PROCEDURES TO REMOVE AND INSTALL REALPORT IN AIX 4.X
----------------------------------------------------------------------------

To remove Realport

	Remove all child process, ttys, lp devices, sa devices.

		pdisable all ttys and stop or remove print queues
		associated with the lp devices.

		Remove devices through smit or rmdev -l <device> -d

		rmdev -l sa<#> -R -d will remove the sa and all      
		tty and lp devices associated with the sa.

	smit

	Software Installation and Maintenance

	Maintain Installed Software

	Remove Software Products

		SOFTWARE name

			Enter digiasync.ncxa.obj

		PREVIEW only?

			Type F4 key

			Select no

		Enter
-------------------------------------------------------------

To install driver

	There are two Realport drivers for AIX 4.X. 4001427E.bin is for    
	AIX version 4.1.X. 4001590A.bin is for AIX version 4.2.X or
	4.3.

	These files as on the ftp server ARE NOT compressed. There is
	no need to execute uncompress or unzip or tar.

	From diskette

		To put the driver file on a diskette

			format /dev/rfd0

			dd if=4001590A.bin of=/dev/fd0 bs=60k

					or

			dd if=4001427E.bin of=/dev/fd0 bs=60k

		To install the driver from diskette

			installp -a all

	From hard drive

		smit

		Software Installation and Maintenace

		Install and Update Software

		Install/Update Selectable Software

		Install Software Products at Latest Level

		Install New Software at Latest Level

			INPUT device / directory for software

				Enter directory where Realport file
				is located

				Enter

			SOFTWARE to install 

				Enter digiasync.ncxa.obj

			COMMIT software updates?

				Type F4 key             

				Select no

				Enter

			SAVE replaced files?

				Type F4 key

				Select yes

				Enter

			Enter