| APPLICATION FOR EQUIPMENT FREQUENCY ALLOCATION | CLASSIFICATION UNCLASSIFIED | DATE | FORM APPROVED OMB No. 0704-0188 Page 1 of 5 Pages |
| --- | --- | --- | --- |
| DOD GENERAL INFORMATION |
| TO | FROM Office of the Army Spectrum Manager \ |
| 1. APPLICATION TITLE Digi International, Inc Models XB24 and XBP24 Transceivers |
| 2. SYSTEM NOMENCLATURE Digi International, Inc Models XB24 and XBP24 Transceivers |
| 3. STAGE OF ALLOCATION (X one) | a. STAGE 1 CONCEPTUAL | b. STAGE 2 EXPERIMENTAL | c. STAGE 3 DEVELOPMENTAL | d. STAGE 4 OPERATIONAL |
| 4. FREQUENCY REQUIREMENTS a. FREQUENCY(IES) 2400 – 2483.5 MHz b. EMISSION DESIGNATOR(S) 2M50G1D |
| 5. TARGET STARTING DATE FOR SUBSEQUENT STAGES |
| a. STAGE 2 n/a | b. STAGE 3 n/a | c. STAGE 4 n/a |
| 6. EXTENT OF USE Intermittent |
| 7. GEOGRAPHICAL AREA FOR |
| a. STAGE 2 n/a |
| b. STAGE 3 n/a |
| c. STAGE 4 US&P, NATO-Member Countries (FMSC#3): (See remarks) |
| 8. NUMBER OF UNITS |
| a. STAGE 2 n/a | b. STAGE 3 n/a | c. STAGE 4 n/a |
| 9. NUMBER OF UNITS OPERATING SIMULTANEOUSLY IN THE SAME ENVIRONMENT 2 |
| 10 OTHER J/F 12 APPLICATION NUMBER(S) TO BE a. SUPERSEDED J/F 12/ 9366 b. RELATED J/F 12/ | 11. IS THERE ANY OPERATIONAL REQUIREMENT AS DESCRIBED IN THE INSTRUCTIONS FOR PARAGRAPH 11? a. YES X b. NO c. NAvail |
| 12. NAMES AND TELEPHONE NUMBERS |
| a. PROGRAM MANAGER | (1) COMMERCIAL | (2) AUTOVON |
| b. PROJECT ENGINEER | (1) COMMERCIAL | (2) AUTOVON |
| 13. REMARKS Item 7c: Afghanistan; Bahrain; Egypt’ Iraq; Kuwait; Oman; Qatar; Saudi Arabia; United Arab Emirates; Japan; Republic of Korea; Australia; New Zealand |
| DOWNGRADING INSTRUCTIONS N/A | CLASSIFICATION UNCLASSIFIED | J/F 12/09366 |
| DD Form 1494, AUG 96 |

| CLASSIFICATION UNCLASSIFIED | PAGE 2 of 5 Pages |
| --- | --- |
| TRANSMITTER EQUIPMENT CHARACTERISTICS |
| 1. NOMENCLATURE, MANUFACTURER’S MODEL NO. XB24 and XBP24 Series | 2. MANUFACTURER’S NAME Digi International, Inc. |
| 3. TRANSMITTER INSTALLATION Ground Vehicles and Building | 4. TRANSMITTER TYPE Phase communication |
| 5. TUNING RANGE 2.405 – 2.480 GHz | 6. METHOD OF TUNING Synthesizer |
| 7. RF CHANNELING CAPABILITY 2450 MHz, 5 MHz Increments | 8. EMISSION DESIGNATOR(S) 2M50G1D |
| 9. FREQUENCY TOLERANCE 40 PPM |  |
| 10. FILTER EMPLOYED (X one) a. YES b. NO |  |
| 11. SPREAD SPECTRUM (X one) a. YES b. NO | 12. EMISSION BANDWIDTH (X and complete as applicable) CALCULATED MEASURED |
| 13. MAXIMUM BIT RATE | a. -3 dB 1.3 MHz |
| 2 Mbps | b. -20 dB 2.8 MHz |
| 14. MODULATION TECHNIQUES AND CODING | c. -40 dB 12.6 MHz |
| OQPSK | d. -60 dB 49.8 MHz |
|  | e. OC-BW 2.5 MHz |
|  | 15. MAXIMUM MODULATION FREQUENCY 2 MHz |
| 16. PRE-EMPHASIS (X one) a. YES b. NO | 17. DEVIATION RATIO (D/R = Max. Freq. Dev/Max. Mod. Freq.) 0.67 |
|  | 18. PULSE CHARACTERISTICS |
| 19. POWER | a. RATE |
| a. MEAN 1mW – 63mW | b. WIDTH |
| b. PEP | c. RISE TIME |
| 20. OUTPUT DEVICE | d. FALL TIME |
| Transistor in IC | e. COMP RATIO |
|  | 21. HARMONIC LEVEL |
| 22. SPURIOUS LEVEL -66 dB | a. 2nd -66 dB |
| 23. FCC TYPE ACCEPTANCE NO. OUR-XBEE and Our-XBEEPRO | b. 3rd -66 dB |
|  | c. OTHER -70 dB |
| 24. REMARKS |
| CLASSIFICATION UNCLASSIFIED | J/F 12/09366 |
| DD Form 1494, AUG 96 |

| CLASSIFICATION UNCLASSIFIED | PAGE 2a of 5 Pages |
| --- | --- |
| TRANSMITTER EQUIPMENT CHARACTERISTICS |
| 1. NOMENCLATURE, MANUFACTURER’S MODEL NO. XB24 and XBP24 Series | 2. MANUFACTURER’S NAME Digi International, Inc. |
| 3. TRANSMITTER INSTALLATION | 4. TRANSMITTER TYPE Digital communication |
| 5. TUNING RANGE 2.4050 – 2.4800 GHz | 6. METHOD OF TUNING Programmable |
| 7. RF CHANNELING CAPABILITY 5000 kHz channel spacing, direct sequence | 8. EMISSION DESIGNATOR(S) 2M32GXW |
| 9. FREQUENCY TOLERANCE 40 PPM (-40C to +85C) |  |
| 10. FILTER EMPLOYED (X one) a. YES b. NO |  |
| 11. SPREAD SPECTRUM (X one) a. YES b. NO | 12. EMISSION BANDWIDTH (X and complete as applicable) CALCULATED MEASURED |
| 13. MAXIMUM BIT RATE | a. -3 dB Not characterized |
| 250 kbps, 8cpb, 2000kcps | b. -20 dB Not characterized |
| 14. MODULATION TECHNIQUES AND CODING | c. -40 dB Not characterized |
| OQPSK with half sine filtering | d. -60 dB Not characterized |
|  | e. OC-BW Not characterized |
|  | 15. MAXIMUM MODULATION FREQUENCY 250Kbps |
| 16. PRE-EMPHASIS (X one) a. YES b. NO | 17. DEVIATION RATIO (D/R = Max. Freq. Dev/Max. Mod. Freq.) 0.5/2450 |
|  | 18. PULSE CHARACTERISTICS |
| 19. POWER | a. RATE |
| a. MEAN 0.0028 W | b. WIDTH |
| b. PEP | c. RISE TIME |
| 20. OUTPUT DEVICE | d. FALL TIME |
| Transistor in IC | e. COMP RATIO |
|  | 21. HARMONIC LEVEL |
| 22. SPURIOUS LEVEL Compliant with FCC 15.247 | a. 2nd Compliant with FCC 15.247 |
| 23. FCC TYPE ACCEPTANCE NO. OUR-XBEE2 | b. 3rd Compliant with FCC 15.247 |
|  | c. OTHER |
| 24. REMARKS |
| CLASSIFICATION UNCLASSIFIED | J/F 12/09366 |
| DD Form 1494, AUG 96 |

| CLASSIFICATION UNCLASSIFIED | PAGE 3 of 5 Pages |
| --- | --- |
| RECEIVER EQUIPMENT CHARACTERISTICS |
| 1. NOMENCLATURE, MANUFACTURER’S MODEL NO. XB24 and XBP24 | 2. MANUFACTURER’S NAME Digi International, Inc. |
| 3. RECEIVER INSTALLATION Ground Vehicles and Building | 4. RECEIVER TYPE Single Conversion Sperheterodyne |
| 5. TUNING RANGE 2405 MHz – 2480 MHz | 6. METHOD OF TUNING Synthesizer |
| 7. RF CHANNELING CAPABILITY 2405 MHz, 5 MHz increments | 8. EMISSION DESIGNATOR(S) 2M50G1D |
| 9. FREQUENCY TOLERANCE 40 ppm |  |
| 10. IF SELECTIVITY | 1st | 2nd | 3rd | 11. RF SELECTIVITY (X and complete as applicable) |
| a. -3 dB | 2.1 MHz |  |  | CALCULATED MEASURED |
| b. -20 dB | 5 MHz |  |  | a. -3 dB 120 MHz |
|  |  |  |  | b. -20 dB 180 MHz |
| c. -60 dB | 10 MHz |  |  | c. -60 dB 480 MHz |
| 12. IF FREQUENCY | d. Preselection Type LC Fliter |
| a. 1st 65 MHz | 13. MAXIMUM POST DETECTION FREQUENCY 2.5 MHz |
| b. 2nd | 14. MINIMUM POST DETECTION FREQUENCY n/a |
| c. 3rd | 16. MAXIMUM BIT RATE 2 Mbps |
| 15. OSCILLATOR TUNED | 1st | 2nd | 3rd | 17. SENSITIVITY |
| a. ABOVE TUNED FREQUENCY |  |  |  | a. SENSITIVITY -92dBm |
| b. BELOW TUNED FREQUENCY | x |  |  | b. CRITERIA s/n = 13dB |
| c. EITHER ABOVE OR BELOW THE FREQUENCY |  |  |  | c. NOISE FIG 7dB |
| 18. DE-EMPHASIS (X one) a. YES b. NO | d. NOISE TEMP n/a |
| 19. IMAGE REJECTION 40 dB | 20. SPURIOUS REJECTION 40 dB |
| 21. REMARKS |
|  | J/F 12/09366 |
| DD Form 1494, AUG 96 |

| CLASSIFICATION UNCLASSIFIED | PAGE 3a of 5 Pages |
| --- | --- |
| RECEIVER EQUIPMENT CHARACTERISTICS |
| 1. NOMENCLATURE, MANUFACTURER’S MODEL NO. XB24 and XBP24 | 2. MANUFACTURER’S NAME Digi International, Inc. |
| 3. RECEIVER INSTALLATION | 4. RECEIVER TYPE Superhet |
| 5. TUNING RANGE 2.4050 – 2.4800 GHz | 6. METHOD OF TUNING Programmable |
| 7. RF CHANNELING CAPABILITY 5000 kHz channel spacing, direct sequence | 8. EMISSION DESIGNATOR(S) 2M32GXW |
| 9. FREQUENCY TOLERANCE |  |
| 10. IF SELECTIVITY | 1st | 2nd | 3rd | 11. RF SELECTIVITY (X and complete as applicable) |
| a. -3 dB | N/A |  |  | CALCULATED MEASURED |
| b. -20 dB | N/A |  |  | a. -3 dB Not Characterized |
| c. -45 dB | N/A |  |  | b. -20 dB Not Characterized |
| d. -60 dB | N/A |  |  | c. -60 dB Not Characterized |
| 12. IF FREQUENCY | d. Preselection Type L-C |
| a. 1st | 13. MAXIMUM POST DETECTION FREQUENCY 250 KHz |
| b. 2nd | 14. MINIMUM POST DETECTION FREQUENCY 250 KHz |
| c. 3rd | 16. MAXIMUM BIT RATE 250 kbps |
| 15. OSCILLATOR TUNED | 1st | 2nd | 3rd | 17. SENSITIVITY |
| a. ABOVE TUNED FREQUENCY |  |  |  | a. SENSITIVITY -95dBm (1% PER) |
| b. BELOW TUNED FREQUENCY |  |  |  | b. CRITERIA 99% packet throughput |
| c. EITHER ABOVE OR BELOW THE FREQUENCY |  |  |  | c. NOISE FIG |
| 18. DE-EMPHASIS (X one) a. YES b. NO | d. NOISE TEMP |
| 19. IMAGE REJECTION | 20. SPURIOUS REJECTION >10dB |
| 21. REMARKS |
|  | J/F 12/09366 |
| DD Form 1494, AUG 96 |
| CLASSIFICATION UNCLASSIFIED | PAGE 4 of 5 Pages |
| ANTENNA EQUIPMENT CHARACTERISTICS |
| 1. | a. TRANSMITTING | b. RECEIVING | c. TRANSMITTING AND RECEIVING |
| 2. NOMENCLATURE, MANUFACTURER’S MODEL NO. AZ4-HSM-525 | 3. MANUFACTURER’S NAME MaxStream |
| 4. FREQUENCY RANGE 2.4000 – 2.4835 GHz | 5. TYPE Half Wave dipole |
| 6. POLARIZATION Vertical | 7. SCAN CHARACTERISTICS N/A |
|  | a. TYPE |
| 8. GAIN | b. VERTICAL SCAN |
| a. MAIN BEAM 2.1 dBi | (1) Max Elev |
| b. 1st MAJOR SIDE LOBE N/A | (2) Min Elev |
|  | (3) Scan Rate |
| 9. BEAMWIDTH | c. HORIZONTAL SCAN |
| a. HORIZONTAL 360 degrees | (1) Sector Scanned |
| b. VERTICAL 70 degrees | (2) Scan Rate |
|  | d. SECTOR BLANKING (X one) (1) YES (2) NO |
| 10. REMARKS Item 5: Half Wave Dipole |
| CLASSIFICATION UNCLASSIFIED | J/F 12/09366 |
| DD Form 1494, AUG 96 |

Page  5a  of   5

SAMPLE LINE DIAGRAM

| APPLICATION FOR SPECTRUM REVIEW | CLASSIFICATION: UNCLASSIFIED | PAGE 5 of 5 Pages |
| --- | --- | --- |
| NTIA GENERAL INFORMATION |
| 1. APPLICATION TITLE Digi International, Inc Models XB24 and XBP24 Transceivers |
| 2. SYSTEM NOMENCLATURE Digi International, Inc Models XB24 and XBP24 Transceivers |
| 3. STAGE OF ALLOCATION (X one) |
|  | a. STAGE 1 CONCEPTUAL | b. STAGE 2 EXPERIMENTAL | c. STAGE 3 DEVELOPMENTAL | d. STAGE 4 OPERATIONAL |
| 4. FREQUENCY REQUIREMENTS |
| a. FREQUENCY(IES) 2405 – 2483.5 MHz b. EMISSION DESIGNATOR(S) 2M50G1D |
| 5. PURPOSE OF SYSTEM, OPERATIONAL AND SYSTEM CONCEPTS (WARTIME USE) (X one) a. YES b. NO |
| 6. INFORMATION TRANSFER REQUIREMENTS 250 kbps |
| 7. ESTIMATED INITIAL COST OF THE SYSTEM |
| 8. TARGET DATE FOR |
| a. APPLICATION APPROVAL 01/01/2008 | b. SYSTEM ACTIVATION 02/01/2008 | c. SYSTEM TERMINATION NAvail |
| 9. SYSTEM RELATIONSHIP AND ESSENTIALITY |
| 10. REPLACEMENT INFORMATION |
| 11. RELATED ANALYSIS AND/OR TEST DATA |
| 12. NUMBER OF MOBILE UNITS |
| 13. GEOGRAPHICAL AREA FOR |
| a. STAGE 2 |
| b. STAGE 3 |
| c. STAGE 4 |
| 14. LINE DIAGRAM See page(s) | 15. SPACE SYSTEMS See page(s) |
| 16. TYPE OF SERVICE(S) FOR STAGE 4 | 17. STATION CLASS(ES) FOR STAGE 4 |
| 18. REMARKS |
| DOWNGRADING INSTRUCTIONS N/A | CLASSIFICATION UNCLASSIFIED | J/F 12/09366 |
| DD Form 1494, AUG 96 |

| APPLICATION FOR FOREIGN SPECTRUM SUPPORT | CLASSIFICATION: UNCLASSIFIED | PAGE of Pages |
| --- | --- | --- |
| FOREIGN COORDINATION GENERAL INFORMATION |
| 1. APPLICATION TITLE Digi International, Inc. Models XB24 and XBP24 Transceivers |
| 2. SYSTEM NOMENCLATURE Digi International, Inc. Models XB24 and XBP24 Transceivers |
| 3. STAGE OF ALLOCATION (X one) |
|  | a. STAGE 1 CONCEPTUAL | b. STAGE 2 EXPERIMENTAL | c. STAGE 3 DEVELOPMENTAL | d. STAGE 4 OPERATIONAL |
| 4. FREQUENCY REQUIREMENTS |
| a. FREQUENCY(IES) 2400 MHz 2483.5 b. EMISSION DESIGNATOR(S) 2M50G1D |
| 5. PROPOSED OPERATING LOCATIONS OUTSIDE US&P |
| 6. PURPOSE OF SYSTEM, OPERATIONAL AND SYSTEM CONCEPTS |
| 7. INFORMATION TRANSFER REQUIREMENTS |
| 8. NUMBER OF UNITS OPERATING SIMULTANEOUSLY IN THE SAME ENVIRONMENT |
| 9. REPLACEMENT INFORMATION |
| 10. LINE DIAGRAM See page(s) | 11. SPACE SYSTEMS See page(s) |
| 12. PROJECTED OPERATIONAL DEPLOYMENT DATE |
| 13. REMARKS |
| DOWNGRADING INSTRUCTIONS N/A | CLASSIFICATION UNCLASSIFIED | J/F 12/09366 |
| DD Form 1494, AUG 96 |