TO INSTALL THE REALPORT DRIVER FOR AIX 3.2.5 AND 4.X. ALSO HOW TO
	ADD A PORTSERVER, TTY AND LP DEVICE TO THE SYSTEM.

TO INSTALL DRIVER;

	From unix;

		installp -a all

	From smit

		Software Installation and Maintenance 

		Install and Update Software

		Install/Update Selectable Software

		Install Software Products at Latest Level

		Install New Software Product at Latest Level

			INPUT device / directory for software

				/dev/fd0 for diskette

					or

				Enter directory where driver file is located

			SOFTWARE to install

				digiasync.ncxa.obj

			COMMIT software updates?

				no

			SAVE relpaced files?

				yes

TO ADD PORTSERVER TO SYSTEM;

	smit devices

	Digi Portservers

		Add a Portserver

		Select appropriate PS type that is being added

		INTERNET NAME
		INTERNET ADDRESS

			Enter PS node name or PS IP address, not both

	A sa device will be created for the PS, make sure that it is available

TO ADD TTY DEVICES;

	smit tty

	Add a TTY

	rs232 Asychronous Terminal

	Select appropriate sa device

		Enter appropriate entries then enter to save

TO ADD LP DEVICES;

	smit printer

	Printer/Plotter Devices

	Add Printer/Plotter

	Select appropriate printer

	rs232

	Select appropriate sa device

		Enter appropriate entries then enter to save

TO REMOVE APPLIED DRIVER;

	Remove all associated Realport tty, lp and sa devices;

		rmdev -l <device> -d

	smit

	Software Installation and Maintenance

	Manage Applied Software

	Remove Applied Software Products

	SOFTWARE name

		digiasync.ncxa.obj