Connecting Peripherals 


Connecting to a Modem 

DB-9 Equipped Boards 
To connect a DB-9 equipped board (PC/2e and MC/2e boards, or PC/4e, PC/8e, 
MC/4e and MC/8e boards with DB-9 fanout cable assemblies) to a modem, use 
standard PC modem cables, available from most electronics stores and computer 
dealers. The wiring diagram for a 9-pin to 25-pin modem cable is shown in
Figure 1. 

Figure 1	DB-9 to DB-25 Modem Cable 
  
	        DB-9 Female                DB-25 Male

		DCD  (1)  ---------------  (8)  DCD
		RxD  (2)  ---------------  (3)  RxD
		TxD  (3)  ---------------  (2)  TxD
		DTR  (4)  ---------------  (20) DTR
		 SG  (5)  ---------------  (7)  SG
		DSR  (6)  ---------------  (6)  DSR
		RTS  (7)  ---------------  (4)  RTS
		CTS  (8)  ---------------  (5)  CTS
		 RI  (9)  ---------------  (22) RI
		GND  (Shell)*************Shell) GND
 
                (****** Cable Shield)  
 
Shielded cable must be used to remain in compliance with Part 15 of FCC rules.


DB-25 Equipped Boards 

Figure 2	DB-25 to DB-25 Modem Cable 
  
	        DB-25 Female               DB-25 Male

		GND  (Shell)*************  (1)  GND
		TxD  (2)  ---------------  (2)  TxD
		RxD  (3)  ---------------  (3)  RxD
		RTS  (4)  ---------------  (4)  RTS
		CTS  (5)  ---------------  (5)  CTS
		DSR  (6)  ---------------  (6)  DSR
		 SG  (7)  ---------------  (7)  SG
		DCD  (8)  ---------------  (8)  DCD
		DTR  (20) ---------------  (20) DTR
		 RI  (22) ---------------  (22) RI
 
                (****** Cable Shield)  
 
To connect a DB-25 equipped PC/Xe or MC/Xe (four and eight port versions) 
board to a modem, use a standard "straight-through" cable (see Figure 2) to 
connect the modem to one of the DB-25 connectors on the fan out cable or
connector box. 


RJ-45 Equipped Boards 
The simplest way to connect a modem to a board with RJ-45 connectors is to use 
RJ-45 to DB-25 "Cable Legs", available from DigiBoard. Call DigiBoard Technical
Sales for more information (612) 943-9020. These adapters use 10-pin RJ-45
plugs, and therefore provide full modem support (Ring Indicator and Data
Carrier Detect are only available on 10-pin RJ-45 connectors). 

Figure 3	RJ-45 to DB-25 Modem Cable (10 Wire) 
  
	        RJ-45 10-Pin               DB-25 Male

		 RI  (1)  ---------------  (22) RI
		DSR  (2)  ---------------  (6)  DSR
		RTS  (3)  ---------------  (4)  RTS
		GND  (4)  ***************  (1)  GND
		TxD  (5)  ---------------  (2)  TxD
		RxD  (6)  ---------------  (3)  RxD
		 SG  (7)  ---------------  (7)  SG
		CTS  (8)  ---------------  (5)  CTS
		DTR  (9)  ---------------  (20) DTR
		DCD  (10) ---------------  (8)  DCD
 
                (****** Cable Shield)  
 
If you wish to build your own modem cable, follow the diagram in Figure 3. 


ALTPIN Modem Wiring (RJ-45 Versions) 

10-pin RJ-45 plugs may be difficult to obtain in the retail market; therefore,
most DigiBoard device driver software incorporates an optional feature called
ALT- PIN, which swaps the logical functions of DSR (Data Set Ready) with DCD
(Data Carrier Detect).  When ALTPIN is enabled (see your device driver software 
reference manual for instructions), DCD becomes available on pin 1 of an 8-pin 
RJ-45 connector (equivalent to pin 2 of a 10-pin connector). 

Figure 4	8-Wire Modem Cable for use with ALTPIN Configuration 
  
	        RJ-45 8-Pin                DB-25 Male

		DCD  (1)  ---------------  (8)  DCD
		RTS  (2)  ---------------  (4)  RTS
		GND  (3)  ***************  (1)  GND
		TxD  (4)  ---------------  (2)  TxD
		RxD  (5)  ---------------  (3)  RxD
		 SG  (6)  ---------------  (7)  SG
		CTS  (7)  ---------------  (5)  CTS
		DTR  (8)  ---------------  (20) DTR
 
                (****** Cable Shield)  
 
If you wish to build an 8-wire modem cable for an RJ-45 equipped board, use an 
8-pin RJ-45 plug wired as shown in Figure 4. 


Connecting the DigiBoard to a DTE Device 

A DTE device is a terminal, serial printer, another computer's serial port,
etc.  To connect the PC/Xe or MC/Xe board (which are also DTE devices) to
another DTE device, you need a null modem cable or adapter.   
 
DB-9 Equipped Boards 
Use a standard PC printer cable, or build a cable as shown in Figures 5 or 6. 

Figure 5	9-Pin to 25-Pin Null Modem Cable 
  
	        DB-9 Female               DB-25 Male

		RxD (2)  ------\ /------  (2) TxD
		                X
		TxD (3)  ------/ \------  (3) RxD

		RTS (7)  ------\ /------  (4) RTS
		                X
		CTS (8)  ------/ \------  (5) CTS

		DSR (6)  --*         *--  (6) DSR
		           |         |
		GND (5)  ---------------  (7) GND
		           |         |
		DCD (1)  --*---\ /---*--  (8) DCD
		                X
		DTR (4)  ------/ \------ (20) DTR

		RI  (9)                  (22)  RI

		GND  (Shell)************* (1) GND
 
                (****** Cable Shield)  

Shielded cable must be used to remain in compliance with Part 15 of FCC rules.


Figure 6	9-Pin Null Modem Cable 
  
	        DB-9 Female               DB-9 Male

		RxD (2)  ------\ /------  (2) RxD
		                X
		TxD (3)  ------/ \------  (3) TxD

		RTS (7)  ------\ /------  (7) RTS
		                X
		CTS (8)  ------/ \------  (8) CTS

		DSR (6)  --*         *--  (6) DSR
		           |         |
		GND (5)  ---------------  (5) GND
		           |         |
		DCD (1)  --*---\ /---*--  (1) DCD
		                X
		DTR (4)  ------/ \------  (4) DTR

		RI  (9)                   (9)  RI

		GND  (Shell)************* (1) GND
  

DB-25 Equipped Boards 

Software Handshaking (XON/XOFF) 
In most cases, serial terminals and printers need only a "three-wire"
connection to the PC/Xe or MC/Xe board. All DigiBoard device driver software
supports XON/XOFF (software) handshaking, so the only signal lines necessary
are Transmitted Data (TxD), Received Data (RxD) and Signal Ground (SG). It
may be necessary to disable DCD (Data Carrier Detect) sensing through a
software command-see your DigiBoard device driver software manual for
instructions.  Cables must be shielded to remain in compliance with FCC
certification requirements, and the shield should be connected to Chassis
Ground (GND) at both ends of the cable run. A simple cable for connecting a
terminal or a printer to a DB-25 equipped DigiBoard board is shown in Figure 7. 

Figure 7	Simple Terminal/Printer Cable (DB-25)  
  
	        DB-25 Female              DB-25 Male

		TxD (2)  ------\ /------  (2) TxD
		                X
		RxD (3)  ------/ \------  (3) RxD

		RTS (4)                   (4) RTS
		                
		CTS (5)                   (5) CTS

		DSR (6)                   (6) DSR
		         
		GND (7)  ---------------  (7) GND
		        
		DCD (8)                   (8) DCD
		                
		DTR (20)                 (20) DTR

		RI  (22)                 (22) RI

		GND  (Shell)************* (1) GND

                (****** Cable Shield)  
 
The cable shown in Figure 7 is a three-wire null modem cable_that is, 
Transmitted Data on one end of the cable is connected to Received Data at the 
other end, and vice versa.   

The male DB-25 end can be plugged directly into most serial terminals and 
printers without any adapters.  The female DB-25 end plugs directly into one of 
the DB-25 connectors on the fan out cable or connector box assembly. 


Hardware Handshaking (Ready/Busy) 

Figure 8	Terminal/Printer Cable with DTR Handshaking (DB-25) 
  
	        DB-25 Female              DB-25 Male

		TxD (2)  ------\ /------  (2) TxD
		                X
		RxD (3)  ------/ \------  (3) RxD

		RTS (4)           *-----  (4) RTS
		                  | 
		CTS (5) ------*   *-----  (5) CTS
                              |
		DSR (6)       |           (6) DSR
		              | 
		GND (7)  ---------------  (7) GND
		              | 
		DCD (8)       |           (8) DCD
		              | 
		DTR (20)      *--------- (20) DTR

		RI  (22)                 (22) RI

		GND  (Shell)************* (1) GND

                (****** Cable Shield)  

Most terminals and printers use Data Terminal Ready (DTR) for Ready/Busy 
hardware handshaking. The cable shown in Figure 8 supports this method. 
 
Some Okidata printers use a control signal on pin 11, called Supervisory
Send Data (SSD) instead of DTR.  In this case, simply connect CTS on the
female DB-25 side to pin 11 of the male DB-25, instead of pin 20. 

Other printer manufacturers may use different methods of 
flow control.  Consult your printer's documentation for spe-
cific wiring requirements.


RJ-45 Equipped Boards 

Software Handshaking (XON/XOFF) 
In most cases, serial terminals and printers need only a "three-wire" connec-
tion to the DigiBoard. All DigiBoard device driver software supports XON/XOFF
(software) handshaking, so the only signal lines necessary are Transmitted
Data (TxD), Received Data (RxD) and Signal Ground (SG). It may be necessary to
disable DCD (Data Carrier Detect) sensing through a software command-see your
DigiBoard device driver software manual for instructions. Cables must be
shielded to remain in compliance with FCC certification requirements, and the
shield should be connected to Chassis Ground (GND) at both ends of the cable
run. 

A simple cable for connecting a terminal or a printer to an RJ-45 equipped 
Digiboard is shown in Figure 9. 

Figure 9	Simple Terminal/Printer Cable (RJ-45) 
  
	        RJ-11 4 Pin               DB-25 Male

		GND (1)  ***************  (1) GND

		TxD (2)  ------\ /------  (2) TxD
		                X
		RxD (3)  ------/ \------  (3) RxD

		GND (4)  ---------------  (7) GND

		GND  (Shell)************* (1) GND

                (****** Cable Shield)  

The cable shown is a three-wire null modem cable_that is, Transmitted Data on 
one end of the cable is connected to Received Data at the other end, and vice 
versa.   

The male DB-25 end can be plugged directly into most serial terminals and 
printers without any adapters. The RJ-11 plug fits into the center of the
RJ-45 jack. 


Hardware Handshaking (Ready/Busy) 

Figure 10	Terminal/Printer Cable with DTR Handshaking (RJ-45) 
  
	        RJ-45 8-Pin                DB-25 Male

		DSR  (1)          *------  (4)  RTS
                                  |   
		RTS  (2)          *------  (5)  CTS

		GND  (3)  ***************  (1)  GND

		TxD  (4)  ------\ /------  (2)  TxD
		                 X
		RxD  (5)  ------/ \------  (3)  RxD

		 SG  (6)  ---------------  (7)  SG

		CTS  (7)  ---------------  (20) DTR

		DTR  (8)
 
                (****** Cable Shield)  
 
Some Okidata printers use a control signal on pin 11, called Supervisory
Send Data (SSD) instead of DTR. In this case, simply connect CTS on the
RJ-45 side to pin 11 of the DB-25, instead of pin 20. Other printer
manufacturers may use different methods of flow control. Consult your
printer's documentation for spe- cific wiring requirements.

Most terminals and printers use Data Terminal Ready (DTR) for Ready/Busy 
hardware handshaking.  The cable shown in Figure 10 supports this method. 
 

RS-232 Cables and Connector Options 

Cables 
RS-232 serial interface cables should be shielded, low capacitance cables,
ideally designed specifically for serial data transmission.   
 
Grounding 
The shield should be grounded at both ends of the cable. Chassis Ground-
available on the shell of DigiBoard's DB-25 and DB-9 connectors, and pin 4 of 
our 10-pin RJ-45 connector, is ideal for this purpose. 
 
Environment 
While good shielding provides reasonable protection against "noise" (Electro-
Magnetic Interference, or EMI), cables should still be routed away from noise 
sources wherever possible.  Avoid laying cables in close proximity to transform-
ers, generators, motors, fluorescent lights, etc. 
 
Capacitance vs. Length of Run 
The total capacitance of a cable affects the integrity of transmitted data. 
As a rule of thumb, the total capacitance of a cable (including the connect-
ors) should not exceed 2500 pF. Serial interface cable is usually rated in
pico Farads per foot. Therefore, if a cable has a capacitance of 50 pF/ft,
and the connectors are 100 pF each, the maximum recommended cable length is
46 feet. If the cable is rated at 12.5 pF/ft, the maximum recommended cable
length is 184 feet, and 5 pF/ft cable can be run up to 460 feet. 

In situations where low-capacitance cable is unavailable, or very long cable
runs are required, "short-haul" modems, available from suppliers such as Black
Box, can be used to increase the effective range of the RS-232 interface.
Short-haul modems are similar to standard modems, except that they are
connected directly to each other via a cable instead of going through a
telephone circuit.  

NOTE_Use only externally-powered short-haul modems with DigiBoard products.