|  | Digi Connect® WAN Application Guide: Configure a VPN between Cisco ASA and the Digi Connect WAN |
| --- | --- |

### Introduction

This is an example configuration of configuring an IPsec VPN tunnel from a Digi Cellular VPN device, such as a ConnectPort WAN VPN, to a Cisco ASA-based firewall. Sections in this document are:

- Example diagram and VPN parameters used.

- Cisco VPN configuration settings. Knowledge of Cisco ASA is assumed and required. Digi does not provide support for non-Digi device configuration. Embedded notes help describe the settings.

- Digi cellular device’s IPsec WebUI configuration

- Testing and basic troubleshooting

### 1.	Example Diagram and VPN Parameters

VPN Parameters:

- Identity: Mobile IP address

- Pre-Shared Key: 1s3d4f5g

- Main mode

- Encryption/Hash transforms: 3des/md5; des/MD5

- Diffie-Helman Group: 2, Perfect-Forward Secrecy (PFS) enabled

- SA Lifetime 86400 seconds.

### 2.	Cisco Sample Config File:

This configuration file describes how to setup a configuration to create a peer to peer VPN connection with a Digi Connect VPN.  The configuration below is for a Cisco ASA which is at the factory default settings.

ASA Version 7.2(3)

!

hostname ciscoasa

domain-name default.domain.invalid

enable password shlxHOGhGlncPVRr encrypted

names

!

interface Vlan1

nameif inside

security-level 100

ip address 172.10.20.1 255.255.255.0

!

interface Vlan2

nameif outside

security-level 0

ip address 209.123.123.123 255.255.255.0

!

interface Ethernet0/0

switchport access vlan 2

!

interface Ethernet0/1

!

interface Ethernet0/2

!

interface Ethernet0/3

!

interface Ethernet0/4

!

interface Ethernet0/5

!

interface Ethernet0/6

!

interface Ethernet0/7

!

passwd shlxHOGhGlncPVRr encrypted

ftp mode passive

dns domain-lookup outside

dns server-group DefaultDNS

domain-name default.domain.invalid

access-list inside_nat0_outbound extended permit ip 172.10.20.1 255.255.255.0 192.168.1.0 255.255.255.0

access-list outside_2_cryptomap extended permit ip 172.10.20.1 255.255.255.0 192.168.1.0 255.255.255.0

pager lines 24

logging enable

logging asdm informational

mtu inside 1500

mtu outside 1500

icmp unreachable rate-limit 1 burst-size 1

asdm image disk0:/asdm-523.bin

no asdm history enable

arp timeout 14400

global (outside) 1 interface

nat (inside) 0 access-list inside_nat0_outbound

nat (inside) 1 0.0.0.0 0.0.0.0

route outside 0.0.0.0 0.0.0.0 209.123.123.123 1

timeout xlate 3:00:00

timeout conn 1:00:00 half-closed 0:10:00 udp 0:02:00 icmp 0:00:02

timeout sunrpc 0:10:00 h323 0:05:00 h225 1:00:00 mgcp 0:05:00 mgcp-pat 0:05:00

timeout sip 0:30:00 sip_media 0:02:00 sip-invite 0:03:00 sip-disconnect 0:02:00

timeout uauth 0:05:00 absolute

http server enable

http 172.10.20.1 255.255.255.0 inside

no snmp-server location

no snmp-server contact

snmp-server enable traps snmp authentication linkup linkdown coldstart

crypto ipsec transform-set ESP-3DES-MD5 esp-3des esp-md5-hmac

crypto map outside_map 2 match address outside_2_cryptomap

crypto map outside_map 2 set pfs

crypto map outside_map 2 set peer 166.122.222.111

crypto map outside_map 2 set transform-set ESP-3DES-MD5

crypto map outside_map 2 set nat-t-disable

crypto map outside_map interface outside

crypto isakmp identity address

crypto isakmp enable outside

crypto isakmp policy 10

authentication pre-share

encryption 3des

hash md5

group 2

lifetime 86400

crypto isakmp am-disable

telnet timeout 5

ssh timeout 5

console timeout 0

dhcpd dns 205.171.3.65 205.171.2.65

dhcpd auto_config outside

!

dhcpd address 172.10.20.2-172.10.20.33 inside

dhcpd enable inside

!

!

class-map inspection_default

match default-inspection-traffic

!

!

policy-map type inspect dns preset_dns_map

parameters

message-length maximum 512

policy-map global_policy

class inspection_default

inspect dns preset_dns_map

inspect ftp

inspect h323 h225

inspect h323 ras

inspect rsh

inspect rtsp

inspect esmtp

inspect sqlnet

inspect skinny

inspect sunrpc

inspect xdmcp

inspect sip

inspect netbios

inspect tftp

!

service-policy global_policy global

group-policy DfltGrpPolicy attributes

banner none

wins-server none

dns-server none

dhcp-network-scope none

vpn-access-hours none

vpn-simultaneous-logins 3

vpn-idle-timeout none

vpn-session-timeout none

vpn-filter none

vpn-tunnel-protocol IPSec

password-storage disable

ip-comp disable

re-xauth disable

group-lock none

pfs enable

ipsec-udp disable

ipsec-udp-port 10000

split-tunnel-policy tunnelall

split-tunnel-network-list none

default-domain none

split-dns none

intercept-dhcp 255.255.255.255 disable

secure-unit-authentication disable

user-authentication disable

user-authentication-idle-timeout 30

ip-phone-bypass disable

leap-bypass disable

nem disable

backup-servers keep-client-config

msie-proxy server none

msie-proxy method no-modify

msie-proxy except-list none

msie-proxy local-bypass disable

nac disable

nac-sq-period 300

nac-reval-period 36000

nac-default-acl none

address-pools none

smartcard-removal-disconnect enable

client-firewall none

client-access-rule none

username digi password anNFDP3Oc4IPXwGS encrypted

tunnel-group 166.122.222.111 type ipsec-l2l

tunnel-group 166.122.222.111 ipsec-attributes

pre-shared-key digi

peer-id-validate nocheck

isakmp keepalive disable

prompt hostname context

no compression svc http-comp

Cryptochecksum:23db5f3182915a51e6bfbf8dfba39138

: end

### 3.	Digi VPN Config:

- Using a browser, access the Digi’s WebUI (e.g. http://192.168.1.1)

- In the left column, select “Configuration” -> “Network”

- Select the “Virtual Private Network (VPN) Settings” link in the middle of the page.

- Select the first link ("VPN Global Settings")

- Miscellaneous Settings: select "Suppress Delete Phase 1 SA Messages For PFS"

- Click “Apply”

- Select "VPN Policy Settings" link just below the Apply button. (Make sure you clicked the Apply button as mentioned above or your changes will be lost).

  - Remove any unneeded tunnels by selecting the "delete" link.

  - Click "Add" to add a new tunnel

  - Enter the WAN IP address or hostname of the Cisco router at the other end of the tunnel, in this example 209.123.123.123.  The IP address must usually be a public IP address reachable from the wireless address of the Digi Connect unit.

- Under "VPN Tunnel:"  Select "ISAKMP"

- Under "Identity: " Select "Use the Interface IP address"

- Under "Local Endpoint":

  - Verify the IP address corresponds to the subnet of the local Ethernet address (in this case 192.168.1.0/255.255.255.0).  If the address is not the same, change the local Ethernet IP address/subnet to the proper address under the Configuration->Network link on the left side of the page.

  - Verify the subnet mask is appropriate for the tunnel you want to create.

  - Note that the IP address and subnet mask define the SOURCE address range for traffic that will be sent through the tunnel from the remote network.

  - Under "Remote Endpoint":

  - Enter the IP address of the network that the data will be flowing TO.  This is the network part of the address that is defined on the LOCAL side of the Cisco Router. In this case 172.10.20.0.

  - Enter the appropriate Subnet Mask that defines the LOCAL side of the Cisco PIX – in this case 255.255.255.0.

- Under the heading: "Use the following IP address, FQDN, or username for the remote VPN’s ID":

      a.  Enter the IP address of the remote Cisco VPN. (209.123.123.123)

- Under the heading: "Use the following pre-shared key to negotiate IKE security settings":

      a. Enter the secret key. In this example it is "digi"

- Under the heading: "ISAKMP Phase 1 Settings":
     
     a.    Select "MAIN" as the connection mode.
     b.    Enable the option "Enable Perfect Forward Secrecy (PFS)

- Under the heading: "ISAKMP Phase 1 Policies" select:

     a.    "Authentication": Pre-Shared-Key
     b.    "Encryption": 3-DES(192)
     c.    "Integrity": MD5
     d.    "SA Lifetime": 86400 secs
     e.    "Diffie-Hellmann": Group 2. Click "Add".

- Under the heading: "ISAKMP Phase 2 Settings" select:

     a.    "Diffie-Hellmann": Group 2

- Under the heading: "ISAKMP Phase 2 Policies" select:

      a.    "Encryption": 3-DES
      b.    "Authentication": MD5
      c.    "SA Lifetime": 28200 secs. Click "Add".

- Click “Apply” to save the information.

The Digi VPN configuration is now complete.

### 4.	Testing and Basic Troubleshooting

Note the tunnel does not come up automatically.  You can attempt to make the tunnel come up by selecting the "Administration > System Information"

- Select the Diagnostics link at the bottom of the page.

- Enter an IP address of a host on remote end of the tunnel (the local side of the Cisco router), e.g. 172.10.20.1.  The IP address needs to be an actual interface IP address.  Click on the Ping button.  Wait for the connection to respond correctly.

- If you do not get a valid response, verify that the IP address is pingable (not filtering ICMP).

- Check the Cisco PIX logs. (As of this writing the Digi has no VPN logs)

- You can check the status from the command line via the “display vpn” command.

### 5.	Where to Get More Information

Refer to the Digi Connect WAN user documentation and Digi technical support website at www.digi.com/support for more information. Technical assistance is available at http://www.digi.com/support/eservice/eservicelogin.jsp.

For sales and product information, please contact Digi International at 952-912-3444 or via www.digi.com.