Software Manual DigiBoard PC/Xe and MC/Xe 
Intelligent Asynchronous Serial Communications Boards 

MS-DOS Introduction 
This MS-DOS device driver supports only application programs that use BIOS 
Interrupt 14h functions to communicate with the board. Programs that
specifically support the basic Interrupt 14h functions 0-3, or DigiBoard's
extended  Interrupt 14h functions, should also work with the boards. 
Most DOS application programs communicate with serial ports by directly 
controlling the interface hardware, and make no attempt to access a device
driver. Because DigiBoard intelligent serial boards do not support virtual-
ization of UARTs, communication with and through the board must be performed
via the DigiBoard device driver. Application programs not specifically written
to support DigiBoard intelligent serial boards may not work with these boards.

Installation Guide. 
 
Device Driver Configuration 
This section describes the installation and configuration of the DOS device
driver.  The procedures described are used for the first-time configuration
of the driver, as well as any future reconfiguration.  You may place the files
in the root (\) directory, or a subdirectory of your choice. An example follows: 
C:\> MD DIGI 
C:\> CD DIGI 
C:\DIGI> COPY A:\DOS\XIDOS5.PGM 
C:\DIGI> COPY A:\DOS\XIDOSCFG.EXE 
C:\DIGI> XIDOSCFG 
The set-up program will configure the DOS device driver so that it can 
communicate with the boards you have installed, and set the parameters the
boards will use to communicate with remote serial devices. The set-up
program modifies XIDOS5.PGM and writes it back to the disk as XIDOS5.SYS. 

The following pages describe the use of the set-up program, XIDOSCFG.EXE. 
 
Micro Channel Board Parameters 
If you are installing a Micro Channel board (MC/Xe, MC/Xi), the configuration 
program will automatically find the memory and I/O port addresses, the IRQ and 
number of channels for each board from the PS/2's Programmable Option Select 
(POS).  Your initial screen will look something like the example shown below. 
   
                   DigiBoard CONFIGURATION PARAMETERS

    Board   Type  Window   Memory   I/O   IRQ   # Brd   Start   Driver
      #            Size    Window   Port   #    Chnls   Chnl#   Support
    ========================================================================
      1     MC/Xi   32k    C8000h   118    4      8       4     DOS/EBIOS
      2     MC/Xe    8k    D0000h   128   11      2      12     DOS/EBIOS
   |_______________________________________________________________________|

    Configuration Selections:                   Use Arrow Keys < >

    Q>uit   C>hannel Parameters   O>ptions   A>dd Board   R>emove Board
    Enter Selection:
	
To change board parameters, you must boot your system with the IBM Reference 
Diskette, and run the configuration program. To change channel parameters,
options, starting channel number and driver support.

ISA Board Parameters 
If you are installing an ISA (PC/Xe, PC/Xi or COM/Xi) board, you will see a 
screen similar to the example below. 
 
                   DigiBoard CONFIGURATION PARAMETERS

    Board   Type  Window   Memory   I/O   IRQ   # Brd   Start   Driver
      #            Size    Window   Port   #    Chnls   Chnl#   Support
    ========================================================================
                        Driver configured for 0 boards 
   |_______________________________________________________________________|

    Configuration Selections:                   Use Arrow Keys < >

    Q>uit   C>hannel Parameters   O>ptions   A>dd Board   R>emove Board
    Enter Selection:
 
The first time you run XIDOSCFG, the parameters will all be empty, because no 
boards have been configured. Select A)dd Board.
You will be presented with three options: A) COM/Xi B) PC/Xe C) PC/Xi 

Choose item that corresponds with your board. 
Your choice will be entered under "Board Type", and you will be prompted for
a memory window size (except COM/Xi boards, which are always 32K).  If your 
board is a newer PC/Xe board (DIP switches on the end of the board), you can 
select an 8K or 64K window.  In most cases, the 8K window is preferable. 

Next, you will be asked to select a starting address for the dual ported memory 
window.  If your board is a newer PC/Xe board (DIP switches on the end of the 
board), the board's address is defined by this step.  If your board is an older
PC/Xe, a PC/Xi or a COM/Xi, choose the address that corresponds to the setting
of the DIP switches or jumpers on the board.  NOTE_if your window size is 8K,
the starting address selection is in two parts: you will first be asked for a
64K segment (e.g. 80000h, C0000h, D0000h), then for the actual starting address
(e.g. D0000h, D20000h, etc.).  All PC/Xe and PC/Xi boards may share the same
starting address.

When asked for the I/O port address, choose the address that corresponds to
the board's DIP switch or jumper setting. Next, enter the IRQ number that you
want assigned to the board (if the board is a COM/Xi, enter the IRQ that is
selected by the jumpers on the board).  In most cases, the IRQ can be disabled.
IRQs are only required for applications which are specifically designed to use
Character Ready interrupts to monitor the board's input buffer status. Finally,
enter the number of channels on the board. See example below: 
 
                   DigiBoard CONFIGURATION PARAMETERS

    Board   Type  Window   Memory   I/O   IRQ   # Brd   Start   Driver
      #            Size    Window   Port   #    Chnls   Chnl#   Support
    ========================================================================
      1     PC/Xi   64k    D0000h   320   10      8       4     DOS/EBIOS
      1     PC/Xe    8k    D0000h   300   15      2      12     DOS/EBIOS
   |_______________________________________________________________________|

    Configuration Selections:                   Use Arrow Keys < >

    Q>uit   C>hannel Parameters   O>ptions   A>dd Board   R>emove Board
    Enter Selection:
 
By using the arrow keys, you can position the highlighted bar over any of the 
parameters for any of the boards.

Channel Parameters and Options (All Boards) 
 
Setting the Starting Channel Number 
The Starting Channel Number (sometimes referred to as DX-LOW) is defined as 
the channel number of the first port on board #1, and is the lowest channel
number that will be supported by the DOS device driver. All ports on all
boards for which the device driver has been configured are numbered sequen-
tially, beginning with the Starting Channel Number.

NOTE:  Standard serial ports (i.e. COM1, COM2, etc.), are numbered beginning 
with 0.  When setting the Starting Channel Number, be sure to account for any 
standard ports that are already installed in your system.  For example, if your 
system has two standard ports, COM1 and COM2, they use channel numbers 0 and 
1.  Start the DigiBoard channels at 2. If your machine has four standard ports, 
COM1-COM4, start the DigiBoard channels at 4 (COM1-COM4 are assigned 
channel numbers 0-3, respectively). 
 
Driver Support 
The DOS device driver can support DOS calling conventions (using a COM name 
such as COM5), Interrupt 14h BIOS calls and EBIOS functions (these functions 
are described in INT14.TXT, in the DOS directory of the distribution diskette). 
Interrupt 14h support is always included in the driver. 

Setting the Channel Parameters 
Channel parameters are set on a board-by-board basis.  To change the channel 
parameters for a board, use the arrow keys to highlight the number of the
board for which you wish to change the parameters, then press the letter "C"
to select C)hannel Parameters.  See the example shown below. 
 
BOARD 1 PARAMETERS 
  CHANL    BAUD      MODE       RX FLOW        TX FLOW        NAME 
 
    4      9600      8,N,1        NONE         DSR/CTS        COM5 
    5      9600      8,N,1        NONE         DSR/CTS        COM6 
 
Q)uit    S)et All                       Use Arrow Keys  * * * * 
Select Parameter : 
 
Use the arrow keys to highlight the parameter you wish to change. In each case 
you will be presented with the available options for that parameter. If you
wish to have the same parameters for all channels, set up one of the channels
in the table as desired, then select S)et All (you need to have the channel
number highlighted). S)et All sets all parameters of all channels to match the
selected channel. 

Baud Rate 
The following baud rates can be specified with the configuration utility:  50, 
75, 110, 134.5, 150, 200, 300, 600, 1200, 1800, 2400, 4800, 9600, 19200, 
38400, 57600, 76800 and 115200. 

Mode 
This parameter defines the character length (5, 6, 7 or 8 bits), type of parity 
checking (odd, even or none) and the number of stop bits (1, 1.5 or 2).  

RX Flow 
Specifies the type of flow control to use for incoming data.  Available options 
are: XON/XOFF (software handshaking), DTR (Data Terminal Ready hardware
handshaking) and RTS (Request To Send_hardware handshaking). These options
may be used singly or in combination. 

TX Flow 
Specifies the type of flow control to use for outgoing data.  Available options 
are: XON/XOFF (software handshaking), CTS (Clear To Send_hardware 
handshaking), DSR (Data Set Ready_hardware handshaking) and DCD 
(Data Carrier Detect_hardware handshaking).  These options may be used 
singly or in combination. 

Name 
Specifies the DOS name (e.g. "COM5") of each port.  This is the name you 
would use in DOS commands such as "COPY FILE.TXT COM5".  If the 
device driver is configured for Interrupt 14h only (see Driver Support, on 
page 27), no name is assigned to the port, and all references must be made by 
BIOS Interrupt 14h calls (BIOS Interrupt 14h functions are described in 
INT14.TXT, in the DOS directory of the device driver distribution diskette). 
 
Enabling/Disabling the Character Ready Flags 
The DOS device driver provides a method of quickly checking the status of the 
input buffers (received data) for an empty or not-empty condition, without
having to set up and execute a BIOS Interrupt 14h function call each time you
want to check. This is done through the Character Ready Flags, which are bytes
in the host computer's RAM (they are located within the body of the device
driver itself), which can be simply checked for a zero or non-zero condition
to determine whether the associated input buffer is empty or not empty,
respectively. 

The FEPOS (Front-End Processor Operating System_the on-board software which 
controls the actual functions of the board) constantly monitors the input
buffers for which Character Ready Flags are enabled, and as soon as a buffer
changes from empty to not empty, the board generates an interrupt request
(IRQ).  The interrupt handler in the DOS device driver sets the appropriate
Character Ready Flag and returns control to the application program, which
must periodically check the flags to see if there is data waiting in the
input buffer.  If a flag is set (non-zero; the byte will actually contain FFh),
there is at least one character in the receiving buffer.  When the last
character has been read from the buffer, the DOS device driver will auto-
matically reset the flag to 00h. 

Since the location of the flags is dependent upon where the DOS device driver
has been loaded in memory, Interrupt 14h, Function 0Dh - Get Pointer to
Character Ready Flag, has been provided (BIOS Interrupt 14h functions are
described in INT14.TXT, in the DOS directory of the device driver distribution
diskette). This function should be run as part of the initialization of any
application program which will use the Character Ready Flags, and since each
channel has its own flag, the function must be run for each channel that will
be monitored via Character Ready Flags. The board and driver must be configured
for an IRQ line for this feature to work. 

To configure the DOS device driver to use the Character Ready Flags, use the 
arrow keys to highlight the number of the board you want to configure, and
select O)ptions from the main menu, then select C)har Ready Flags.  You will
be presented with a screen similar to the example below. 
 
Board 1 Character Ready Flag Status 
 
      Chnl  4 : Disabled        Chnl  5 : Disabled 
      Chnl  6 : Disabled        Chnl  7 : Disabled 
      Chnl  8 : Disabled        Chnl  9 : Disabled 
      Chnl 10 : Disabled        Chnl 11 : Disabled 
Change : 
T)oggle One Channel  E)nable All Channels  D)isable All Channels  Q)uit 
 
To enable or disable the Character Ready Flag for an individual channel, select 
T)oggle One Channel, then enter the number of the channel to be modified. 
 
Enabling/Disabling the Alt Pin Feature 
"Alt Pin" is a special parameter that may be helpful for connecting modems to 
boards equipped with RJ-45 "modular" connectors.  It should not be enabled on 
boards equipped with DB-25 or DB-9 connectors.  Enabling "Alt Pin" causes the 
device driver to internally "swap" the signals DCD (Data Carrier Detect) and
DSR (Data Set Ready).
 
Board 1 Alt Pin Status 
 
      Chnl  4 : Disabled        Chnl  5 : Disabled 
      Chnl  6 : Disabled        Chnl  7 : Disabled 
      Chnl  8 : Disabled        Chnl  9 : Disabled 
      Chnl 10 : Disabled        Chnl 11 : Disabled 
 
Change : 
T)oggle One Channel  E)nable All Channels  D)isable All Channels  Q)uit 
 
To enable or disable Alt Pin for an individual channel, select T)oggle One 
Channel, then enter the number of the channel to be modified.  If previously
disabled, that channel will now be enabled, and vice versa. 

Memory Enable/Disable Option (PC/Xe and PC/Xi Boards) 
PC/Xe and PC/Xi boards' dual-ported memory is "stackable"_that is, all PC/Xe 
and PC/Xi boards in a system can share the same memory addresses, since only
one board's memory is turned on at any given time. The DOS device driver
normally turns a board's memory off after a read or write operation to that
board. To configure the DOS driver to leave the PC/Xe or PC/Xi board's memory
enabled when not in use, highlight the board you wish to change (use the arrow
keys), select O)ptions, then select L)eave Memory Enabled. You will see the
following choices: 
 
Current Status: Leave Memory Disabled. 
 
Leave Memory D)isabled     E)nabled 
Enter Selection 
 
Exiting the Set-Up Program 
Once all of the parameters have been set as desired for each board, exit the
set-up program by selecting Q)uit from the main menu. If the driver is already
loaded and the board(s) are installed, you will be asked: 

Re-configure the Board? (y/*): 
If you answer "yes", the changes will be made to the board and driver, and will 
take effect immediately.  Next, you will be asked: 

Save Changes to Disk for Re-Boot? (y/*): 
Answer "yes" if you wish the changes to become permanent (you must answer 
"yes" if this is the first time you have configured the driver). Now you will
be asked: 

Quit? (Q/*): 
Select "Q" to quit. Any other key will return you to the main menu of the
set-up program. You will be asked: 

Would you like your CONFIG.SYS updated? (y/*) 
Answer "yes" if you want the device driver command line to be added to 
CONFIG.SYS by the configuration program.  If you answer no, you must 
manually update CONFIG.SYS to load the driver (see Loading the Device Driver, 
on the next page). NOTE: If you reconfigure the board without saving the
changes to disk, the changes will be effective only until DOS is rebooted.
The driver will then revert to whatever parameters have been previously set. 

Loading the Device Driver 
Once the driver has been configured and the file XIDOS5.SYS has been created, 
the driver needs to be added to the system configuration.  This was done 
automatically by the configuration program, unless you answered "no" to the 
question "Would you like your CONFIG.SYS updated? (y/*)".  
In this case, you need to add the line  

DEVICE=C:\DIGI\XIDOS5.SYS 

to CONFIG.SYS in the root directory (assuming that you have located the driver 
file in C:\DIGI).  Use your favorite text editor to do this. Now reboot your
computer. When the driver is loaded, the following information should be
displayed (depending upon your system configuration and AUTOEXEC.BAT file, it
may scroll by too quickly to read): 
 
DigiBoard Intelligent DOS Driver Version 4.0.0 
Copyright (C) DigiBoard, Inc. 1991 
 
Board 00 - Initializes Successfully. 
Board 01 - Initializes Successfully. 
(This is what you would see if you had installed two boards.) 
The DOS device driver is now loaded and ready for use. 
 
If your system is running an expanded memory manager (e.g. EMM386, QEMM,
etc.), be sure to exclude the memory address range used by the board (8K,
32K or 64K, depending on the board type). This is usually done with a command
line option in the DEVICE= line for your memory manager in CONFIG.SYS. 
EXAMPLES (EMM386.EXE; boards addressed at D0000h):   

PC/Xe (8K version) 
DEVICE=EMM386.EXE [...] -X D000-D1FF 
PC/Xe (64K version) and PC/Xi (64K) 
DEVICE=EMM386.EXE [...] -X D000-DFFF 
COM/Xi (32K) 
DEVICE=EMM386.EXE [...] -X D000-D7FF 
Consult the documentation for your expanded memory manager 
for instructions.

Uninstalling the Device Driver 
To uninstall the device driver, simply remove the DEVICE= line from 
CONFIG.SYS, and delete the files in C:\DIGI (or whatever directory you 
copied them to). Alternatively, if you just want to temporarily disable
the driver without losing your configuration information, you can "comment
out" the driver by putting "REM" in front of the DEVICE= line in CONFIG.SYS. 

Error Messages 
During the initialization of the DOS device driver and the boards (at boot-up
time), the following messages might appear on your console. 
 
Before calling Technical Support, be sure to run the Memory Map utility to
find the required amount of available address space, and the User Diagnostics
to verify that the board is working correctly.  See the Installation Tips
section of the Installation Guide for your board for details.
 
Board 00 - Port 320h not found. 
The driver was configured for a board with an I/O port at 320h, but could not 
find a board at that address. Verify that the board's DIP switches or jumpers
are set for the correct I/O Port address, as defined with the set-up program
(if the board is an MC/Xe board, check the POS). 
 
Board 00 - Port at 320 fails hardware reset. 
The driver could not reset the board.  This usually indicates a hardware mal-
function, but could also result from an I/O Port address conflict with some 
other device in your system. Reconfigure the board for a different I/O Port
address.  Make sure to run the set-up program to reconfigure the driver
accordingly. 
 
Board 00 - Memory Not Found  
No memory was found at the address specified during driver configuration. 
Make sure that the board is securely seated in the computer's I/O bus slot. 

Board 00 - Fails BIOS Initialization. 
Board 00 - Fails FEPOS Initialization. 
Board 00 - Fails Command Buffer Initialization. 
These messages indicate that the initialization process failed while the driver 
was attempting to load or use on-board code.  Failures of this kind may be 
caused by a board hardware malfunction or by memory address conflicts with 
another device in your system. Try rebooting your system.  If the message
still persists, check your system for possible address conflicts. 
 
Board 00 - Fails IRQ Test - Check IRQ Setting. 
This message indicates the board was initalized properly but interrupts could 
not be generated by the board.  This usually means that there is an IRQ 
conflict with another device in your system. Check and rectify any differences 
or conflicts.  If the error persists, it is probably related to faulty hardware.