Installation Guide 
for DigiBoard EPC/X System 
for SBus Computers Solaris Release 5.x 
DBI 92000147A 

Be sure to read the Release Notes that may be included with 
this software device driver.  The Release Notes contain 
information not available at this manual's press time. 

Software Installation 
 
Software changes more rapidly than printed documentation can keep up. For
this reason, some of the screens or prompts may not appear exactly as shown.
 
Installing the Driver Package 
1.  Log onto the console as super-user (root). 
 
2.  To begin the installation, insert the DigiWARE diskette in the diskette
    drive and enter the command: 

    pkgadd -d diskette1  

This will run the System Administration program designed to assist in Add 
On Package installation. Refer to the Operations/System Administrator's
Guide for more information on pkgadd. 

You will see the following (or something similar): 

-----------------------------------------------------------------------------
|  Installation in progress.  Do not remove the diskette.                   |
|                                                                           | 
|  The following packages are available:                                    | 
|  1.   dgiiepc    DigiBoard Async Driver Package 1.0.0                     |
|                                                                           | 
|  Select package(s) you wish to process (or 'all' to process all packages).| 
|  (default: all) [?, ??, q]                                                |
-----------------------------------------------------------------------------

3.  Press <Enter> to select dgiiepc. 
    You will now see the following (or a similar) screen:		 
 
-----------------------------------------------------------------------------
|  This script installs the DigiBoard EPC/X driver for:                     | 
|                                                                           | 
|       Solaris Rel. 5.1                                                    |  
|                                                                           | 
|  This script also installs the information needed by UNIX to use          |
|  these additional ports.  This driver supports up to 8 Host Adapter       |
|  boards.                                                                  |
|                                                                           | 
|  By default, the ports are installed with the basename "/dev/dty/".       |
|  DigiPrint ports are installed in "/dev/dpr/".                            |
|                                                                           | 
|  Press <CR> to proceed or "Q" to quit:                                    | 
-----------------------------------------------------------------------------
 
Press <Enter>. 
 
4.  The system displays: 
 
-----------------------------------------------------------------------------
|The port names in the /dev directory will look like:                       |  
|                                                                           | 
|       /dev/dty/a001s                                                      |
|                                                                           | 
|  where dty/ is a sub-directory in /dev, "a" is an ID letter               |
|  that can be different for each port box, and "001" is the port number and|
|  the suffix "m" or "s" is "modem" or "standard" tty device.               |
|                                                                           | 
|  Systems with a large number of ports may need to use some letters more   |
|  than once.  When this occurs, the first box to use an ID letter will     |
|  get port numbers 01-16, the second box to use that letter will get       |
|  port numbers 17-32, and so on.                                           | 
|                                                                           | 
|  You can have the install script pick ID letters for you, assigning       |
|  letters consecutively (a, b, c, d...) and starting over from the         |
|  beginning when it runs out of letters; or you can choose them manually.  | 
|                                                                           | 
|  Manual ID selection is recommended for larger systems, where it can be   |
|  used to help keep port names more organized.                             |
|                                                                           | 
|  Do you want ID letters picked for you (y or n)?                          | 
-----------------------------------------------------------------------------
 
If you want the system to arbitrarily assign ID letters to the concentrators 
and PORTS modules, enter "y".  If you want to choose your own ID letters, 
enter "n". 

5.  Now the system displays: 
 
-----------------------------------------------------------------------------
|  How many boards do you wish to install (1-8)?                            | 
-----------------------------------------------------------------------------
 
Enter the number of EPC/X host adapters you have installed in your 
computer. 
 
Steps 6-8 will be repeated for each EPC/X host adapter installed in your sys-
tem. 
 
6.	You will see the display: 
 
-----------------------------------------------------------------------------
|   Configuring board 1. 
|   Board type is SBUS EPC/X Host Adapter. 
|                                                                           | 
|  Line Configuration: 
|   The sync lines may be configured two ways.  The basic method has all 
|   connections wired "8 wire direct" at a speed of either 1228K bps or 
|   10M bps, and can be used for quick set-up for most situations.  The 
|   custom method allows you to choose speeds and wiring methods 
|   individually. 
|                                                                           | 
|       Do you want to use the basic installation method (y or n)?
-----------------------------------------------------------------------------
 
Answer "y" for the basic installation, or "n" if you want to do the custom 
installation. 
 

Basic Configuration (preceed ahead for Custom Configuration) 
7a.  If you chose the basic configuration in Step 6, you will see the
     following screen: 
 
 Configuring board 1. 
 Board type is SBUS EPC/X Host Adapter. 
 
Basic Configuration: 
 
 One of two line speeds must be chosen for the basic configuration 
 method.  The choices are 1228K bps and 10M bps.  Running the sync 
 lines at 1228K bps maintains compatibility with C/CON-16 
 concentrators.  Running the sync lines at 10M bps allows higher 
 performance, but is not compatible with C-CON/16 concentrators and 
 restricts the length of the sync cable.  For more information, see 
 the manual. 
 
        1) 1228K bps 
        2) 10M bps 
 
 Which speed do you wish to run the sync lines at?
 
Select 10M bps only if: 
*	all attached concentrators are EPC/CON-16 concentrators, and  
*	the cumulative length of all daisy chain cables on either 
        sync line is 30 feet or less. 
See the EPC/CON-16 Installation Guide for more detailed 
information about data rates versus cable lengths.

 
7b.  Now you will be asked how many concentrators are attached to each sync 
line, and how many EBI modules are attached to each concentrator (this 
refers to DigiBoard PORTS modules connected to the "EBI Out" port of 
EPC/CON-16 concentrators).  If, in Step 4, you elected to choose your own 
concentrator/PORTS module ID letters, you will also be prompted for the ID 
letters at this time. 

The number of concentrators you specify here must match the node number 
of the last concentrator installed on that sync line (e.g. if you have four 
concentrators, but their node numbers are set to 1, 2, 3 and 5, you must enter 
5 for the number of concentrators).  This applies only to EPC/CON-16 
concentrators and plastic C/CON-16 concentrators.  Metal C/CON-16 
concentrators' node numbers are set automatically by the system.  See the 
Installation Guide for your concentrators for more information on Node 
Numbers. 

Now proceed to Step 8, on page 10. 

Custom Configuration 
The custom configuration requires you to specify the wiring method and the data 
rate for each sync line.  The wiring options are: 
1)	4-wire direct 
2)	8-wire direct 
3)	8-wire synchronous modem 
4)	RS-232 synchronous modem 
The supported data rates are: 
4-wire direct 
	1) 230K	  2) 460K       3) 921K*         4) 1843K* 
8-wire direct 
	1) 2400	  5) 38.4K      9) 230K	        13) 1843K*	17)10M* 
	2) 4800	  6) 57.6K	10) 460K	14) 2458K* 
	3) 9600	  7) 76.8K	11) 921K	15) 3686K* 
	4) 19.2K  8) 115K	12) 1228K	16) 7373K* 
8-wire synchronous modem 
	1) 2400	  6) 38.4K	11) 460K 
	2) 4800	  7) 57.6K	12) 921K 
	3) 9600	  8) 76.8K	13) 1228K 
	4) 14.4K  9) 115K 
	5) 19.2K 10) 230K 
8-wire RS-232 synchronous modem 
	1) 2400	  4) 14.4K	7) 57.6K 
	2) 4800	  5) 19.2K	8) 64.1K 
	3) 9600	  6) 38.4K	9) 76.8K 

*  Rates with an asterisk are incompatible with C/CON-16 concentrators. These 
data rates can only be used if all concentrators on a given sync line are 
EPC/CON-16 concentrators.  Also, see Restrictions on Cable Lengths in the 
EPC/CON-16 Installation Guide and Reference Manual. 

8.  You will now be asked to confirm the configuration for the board.  
Depending on your configuration, you might see something like this: 
 
You have selected the following configuration for board 1: 
    SBUS EPC/X Host Adapter. 
 
       Connections     Speed     Cabling         Port Names 
     ------------------------------------------------------------------- 
         Line 1 
      Concentrator 1    10M      8 wire direct dty/a001[ms] - dty/a016[ms] 
        EBI Module 1                           dty/b001[ms] - dty/b016[ms] 
        EBI Module 2                           dty/c001[ms] - dty/c009[ms] 
      Concentrator 2    10M      8 wire direct dty/d001[ms] - dty/d016[ms] 
        EBI Module 1                           dty/e001[ms] - dty/e016[ms] 
        EBI Module 2                           dty/f001[ms] - dty/f016[ms] 
        EBI Module 3                           dty/g001[ms] - dty/g008[ms] 
      Concentrator 3    10M      8 wire direct dty/h001[ms] - dty/h016[ms] 
      Concentrator 4    10M      8 wire direct dty/i001[ms] - dty/i016[ms] 
 
         Line 2 
      Concentrator 1    10M      8 wire direct dty/j001[ms] - dty/j016[ms] 
      Concentrator 2    10M      8 wire direct dty/k001[ms] - dty/k016[ms] 
      Concentrator 3    10M      8 wire direct dty/l001[ms] - dty/l016[ms] 
      Concentrator 4    10M      8 wire direct dty/m001[ms] - dty/m016[ms] 
        EBI Module 1                           dty/n001[ms] - dty/n009[ms] 
 
  Is this configuration acceptable (y or n)?

 
If you accept the configuration, Steps 6-8 will be repeated for each additional 
board specified in Step 5.  Otherwise, you will be returned to Step 6 (page 7) 
to re-enter the configuration for the current board. 
 
9.  Next, you need to select the altpin setting. This allows alternate wiring of
the RJ-45 modular connectors.  The default for altpin is OFF, giving you the 
standard DigiBoard RJ-45 pinouts.  Setting altpin to ON enables the 
alternate RJ-45 pinouts. 

The following message will be displayed: 
 
        Altpin is provided to allow the DCD input signal to be exchanged 
        with the DSR input.  This is useful on products with RJ-45 
        connectors as these products have DCD on pin 10.  Choosing 
        altpin will allow the use of 8-pin connectors while still having 
        the benefit of full modem control.  The use of "altpin" on 
        products with DB-25 connectors is not normally recommended. 
 
The default setting for altpin is off. 
Is this acceptable (y or n)?

Answer y or n as appropriate. 
Note that answering "n" here activates the altpin configuration for all ports 
on that board.  Individual ports can be set with ditty. 

Creating New Devices 
Devices will now be created in /dev/dty,  and /dev/dpr, giving Solaris the 
information to use the additional ports. 
The DigiBoard driver will support up to 8 EPC/X host adapters.   
EPC/X host adapters can each have up to 14 concentrators and/or PORTS/em 
modules attached for a total of 1792 asynchronous ports per system (8 host 
adapters).  The maximum number of concentrators per synchronous line is eight.  
PORTS/em modules may be attached to the concentrators, as long as the total 
number of boxes (concentrators and PORTS modules) does not exceed 14. 
The devices are named according to the following conventions: 
 
Format used for port names 
 
/dev/dty/	
Directory path for tty devices. 
 
/dev/dpr/	
Directory path for transparent printer devices. 
 
a-n     Concentrator or PORTS module letter I.D.  Legal letters are a-n. 

001-128 Port number on the individual concentrator or PORTS module.   
 
s, m	Indicates whether port is a "standard" (s) or "modem" (m) port.  
        Modem ports can only be opened when Data Carrier Detect (DCD) is 
        active. For example, standard tty port 4 on concentrator or PORTS
        module "b"  will be /dev/dty/b004s. The same port with modem control
        enabled would be named /dev/dty/b004m. Similarly, transparent printer
        ports will be named /dev/dpr/b004s or /dev/dpr/b004m. 

NOTE:  A port may be enabled as either a standard or modem tty device, but 
not both.

Loading the Driver 
You will see the following (or similar) message: 
 
epca    ports=202   SBus EPC/X V 1.0.0 

 
If there is a problem with the board or the driver configuration, you may see
error messages after this screen_see page 28 for explanations of the error
messages that may occur. If no errors are detected, EPC/X host adapters will
proceed to download the operating software to the C/CON-16 and/or EPC/CON-16
concentrators. Once the concentrators are running, their displays will show
"AC". It is not necessary to reboot after the initial installation, but it is
encouraged, to be certain that the driver is properly installed. When the
system is rebooted, the driver will be force loaded and the above message
will be seen if all is well. 
 
ditty options set from an rc script must be set after the download program
has run, and must wait for the board to boot before running. ditty options
should be added to the end of /etc/rc2.d. This can be done by giving it a
name such as "S99epc" or "S99dittystuff", where the "S" must be a capital
letter, and the greater the number, the later the script is run. For example,
to set altpin for port a001s, add the following line to
/etc/rc2.d/S99dittystuff: /usr/bin/ditty altpin /dev/dty/a001s

Enabling the New Ports 
Please refer to your Solaris System Administrator's Guide, under the Peripherals
Setup section, for the details on how to enable serial ports.  The following 
example shows how to set up serial ports for use with terminals: 
 
1.  Connect terminals to the ports (using a null modem, if necessary) and test 
the connections to each terminal by entering the following command for each
port added: 
 
date > /dev/dty/a001s 
 
(Assuming the terminal is connected to a001s.) 
Please note that in the above, the "date" command is used as a simple test, 
to provide text output that can be redirected; there is no other significance 
to "date" in this test. 
*  If the date appears on the terminal's screen, the device is properly 
   connected. 
*  If the date does not appear on the terminal's screen, then that terminal is 
   not receiving data; check the power, cables, connections, etc. 
*  If nonsense characters are printed on the terminal's screen, check the 
   baud rates, data bits, stop bits, and parity setting on your terminal.   
   Once you can redirect output to a terminal with the test above, perform the 
   following steps to enable that port. 
 
2.  Log onto the console as super-user (root). 
 
3.  Enter (on a single command line): 
    pmadm -a -p ttymonx -s a001s -fu -i root -v `ttyadm -V`\  
    -m "`ttyadm -d /dev/dty/a001s -l 9600 -s /usr/bin/login`" 
    where ttymonx is the port monitor tag.  This will enable the port suitably 
    for a terminal.  For more information, see ttymon and ttyadm in the 
    Answer Book. 


Un-Installing the Device Driver 
Enter the following commands to un-install the device driver software: 
 
1.  Log onto the console as super-user (root). 
 
2.  Enter the following command: pkgrm 
 
A list of installed packages will be presented. Choose the dgiiepc package.  
The package containing the driver will now be removed from the system. In
the event that some of the ports were open when pkgrm was initiated, the 
unloading of the driver will fail. In this case it will be necessary to reboot
to complete the driver removal. 


DigiBoard TTY Devices 
This device driver supports three different UNIX devices on each line. On line 
"a001," where "a" refers to concentrator a, and "001" refers to first line
(port) on that concentrator, there are three devices: 

/dev/dty/a001m 
The "modem" tty device, used for terminals, modems, printers, laboratory 
equipment, etc.  This is also sometimes referred to as a "dial-in" device. 
This is a traditional UNIX port with modem control.  It requires Carrier Detect 
to be high before it will operate. RTS/CTS handshaking is enabled by default. 
When used with a modem, the port will wait for carrier before sending out 
the login: prompt, so the user is greeted properly upon making a connection.   
When used with a terminal or other device, it is usually wise to wire the 
DigiBoard DCD signal to the terminal's DTR (Data Terminal Ready) line.  
When the terminal is turned on, the system outputs a login: prompt.  
When the terminal is turned off, any associated jobs are killed, and the user 
is logged out.  
 
/dev/dty/a001s 
Standard device. This is the same as /dev/dty/a001m with the excep-
tions that the default handshake method is XON/XOFF, and that Data 
Carrier Detect need not be present to open the device.  Once a connection is 
established and DCD becomes active, standard devices behave in the same 
way as modem devices_subsequent loss of the Data Carrier Detect signal 
will cause the jobs to be killed and the user will be automatically logged 
off. 

/dev/dpr/a001s, /dev/dpr/a001m 
The "Transparent Print Devices" (DigiPrint ) for use with the auxiliary printer 
port of a terminal. Output directed to a transparent print device goes out the 
auxiliary port of a terminal while the user continues to use the terminal 
normally. 
Transparent print devices allow you to use your terminal and a local printer 
connected to the terminal's auxiliary port at the same time.  The system 
assumes data you send to the dpr device is destined for the printer. Before 
sending data to the printer, the system sends a special control sequence to 
the terminal to activate the printer port, sends the data, then turns the
printer port back off again before sending more data for the terminal. 
For correct operation, several parameters must be provided to the ditty 
program.  It is usually best to set these up in /etc/rc2.d, since they 
must be set each time the system is rebooted.  See Setting Terminal Options 
with ditty (page 18) and DigiPrint  Transparent Print Option (page 24). 
An example setup line in one of the /etc/rc files might be:     
 
ditty term wyse60 maxcps 80 bufsize 2000 maxchar 50 
/dev/dty/a001s  
 
Error Messages 
The following error messages are generated by the driver: 
 
WARNING: EPC/X memory allocation error. <2> 
What it means: The operating system would not allocate memory to the driver. 
Action to take: Adjust kernel resources. 
 
WARNING: EPC/X not resetting. <3> 
What it means: The board doesn't respond to reset. 
Action to take: Make sure the board is fully seated in the slot. 
                Potential hardware problem. 
 
WARNING: EPC/X: No memory at 0xXX <4>. 
What it means: The driver cannot read the board's dual ported memory. 
Action to take: 
Make sure the board is fully seated in the slot. Make sure the board settings 
and driver settings match.  Potential hardware problem. 

WARNING: EPC/X: port X failed diagnostics <5>. 
What it means: The driver encountered an error executing on-board BIOS. 
Action to take: Potential software problem. 
 
WARNING: EPC/X  FEPOS not functioning. <7> 
What it means: The driver encountered an error executing on-board FEPOS. 
Action to take: Potential software problem.  Potential hardware problem. 
 
EPC/X: found X card(s), expected Y card(s). <6> 
What it means: The driver was configured for Y boards and only found X boards. 
Action to take: Make sure boards are fully seated in slots. 
                Potential hardware problem.