Installation Guide for 
DigiBoard PC/Xe and PC/Xi 
Intelligent Communications Boards 
UNIX System V/386, Release 4 
Solaris x86, Version 2.x 
Wyse MP System V/386, Release 4 
DBI 92000097D 

Introduction 
The DigiBoard device driver software for System V/386, Release 4, Solaris x86, 
Version 2.x and Wyse MP System V/386, Release 4 is an installable device driver
the software development system is not required to create a new kernel. 

Software Installation 
 
Installing the Driver Package 
1.  Log onto the console as super-user (root). 
 
2.  To begin the installation, load the device driver diskette into drive
    A and type: pkgadd -d diskette1 

(If you wish to load the driver from drive B, substitute "diskette2" for 
"diskette1" in the above command.) 
 
3.  Next, you must answer a series of questions about the installation.  In
each case, options will be presented and/or examples will guide you in
answering the questions. The driver supports up to four PC/X* boards, with
up to sixteen ports each. You will see the screen: 
 
The DigiBoard PC/X* driver may be installed using one of the four 
suggested configurations listed below, or you may choose to create your 
own custom configuration. 
 
        1) I/O Port=0x320, Memory Address=0x000D0000 
        2) I/O Port=0x300, Memory Address=0x00F00000 
        3) I/O Port=0x220, Memory Address=0x000D0000 
        4) I/O Port=0x120, Memory Address=0x00F00000 
        5) Custom or multiple board installation. 
        6) Exit installation procedure. 
 
        Please enter selection (1-6)?
 
When asked, select your configuration from the above list (1-5), or choose 
option 6 to abort the device driver installation.  
Note that options 1 through 4 are for installing single boards only!  If you
are installing two, three, or four boards, or wish to set up one board with
parameters different from those above, choose #5.  
For any of the versions selected, the corresponding DIP switches on the PC/X* 
board must be set to match the parameters listed in the configurations above.   
If you selected Option 5, the next prompts you will see will be for Custom 
Configuration Instructions.  If you answered 1-4, skip to Step 10 on page 
11. 
 
4.	The software displays: 
 
Each DigiBoard PC/X* board requires an I/O port address and a 64K to 512K 
block of memory.  Please select these to avoid conflicts with other boards 
you may have installed in your system. 
 
How many PC/X* boards do you wish to install (1-4)?

 
Enter in the number of PC/X* boards you are installing. 
 
Steps 5-8 are repeated for each of the boards you specified in Step 4. 
 
5.   You must select a Port address for each board. The software displays
     the Port address options.  
 
Ready to configure board #1. 
=========================== 
 
        The I/O port address choices, in hexadecimal, are: 
                100     200     300 
                110     220     320 
                120 
        Please enter selection (100-320):

 
Make your selection by entering one of the numbers shown above. 
 

6.   The next item requires the selection of the host starting address of
the board's dual-ported memory (all boards can operate at the same Memory
Start address, if desired).  The software lists the available Memory Start
address options: 
 
The memory address choices, in hexadecimal, are: 
                08) 0x00080000  0E) 0x000E0000  E8) 0x00E80000 
                09) 0x00090000  D0) 0x00D00000  F0) 0x00F00000 
                0C) 0x000C0000  D8) 0x00D80000  F8) 0x00F80000 
                0D) 0x000D0000  E0) 0x00E00000 
        Please enter selection code (08-F8):
 
When asked, enter your selection (08-F8). 
 
7.	The software then asks: 
 
Please indicate number of ports on board #1 (2, 4, 8, or 16):

 
Answer 2, 4, 8 or 16 as appropriate for the number of channels on the 
DigiBoard product you are installing. 
 
8.  Next, you need to select the altpin setting.  This allows alternate
wiring of the RJ-45 modular connectors.  Setting altpin to "OFF" gives you
the standard DigiBoard RJ-45 pinouts.  Setting altpin to "ON" enables
alternate RJ-45 pinouts.  (This is useful for 8-pin RJ-45 connectors. 
See the Installation Guide for your board for more details.

The software asks: 
 
Do you want to set altpin for this board? (y or n)

Answer y or n as appropriate. 
Note that this sets all ports to altpin.
 
Steps 5-8 will be repeated for each PC/X* board you specified in Step 4. 
 

9.  You will now be asked to confirm your selections. Depending upon the
version of your operating system, you will see one of the following screens
(or the equivalent, reflecting your configuration): 
 
You have selected the following configuration: 
 
        Board   I/O Address   Memory Address   Devices 
        ----------------------------------------------------- 
         1        0x100        0x000D0000      term/i1a - term/i1h 
                               Modem devices:  term/i1A - term/i1H 
         2        0x200        0x000D0000      term/i2a - term/i2h 
                               Modem devices:  term/i2A - term/i2H 
         3        0x300        0x000D0000      term/i3a - term/i3p 
                               Modem devices:  term/i3A - term/i3P 
         4        0x110        0x000D0000      term/i4a - term/i4p 
                               Modem devices:  term/i4A - term/i4P 
 
        Is this configuration acceptable (y or n)?

 
If the information is correct, answer "y."  Otherwise, answer "n" and the 
software will let you start over again with Step 4. 
 
10.	Finally, the software asks: 
 
Are you installing on a machine with cache enabled (y or n)?

 
Enter "y" only if the cache on your machine can be disabled through software.  
For any other machine with memory cache, press "n" and check with your 
system manufacturer for information on working with that machine's cache.  
You may have to choose a Memory Start address below 1 megabyte to avoid 
conflicts.  
Call DigiBoard Technical Support, at (612) 943-9020 if you need more 
information. 


Next, the installation script creates devices in /dev, giving UNIX the
information to use these additional ports. The DigiBoard driver will
support up to four PC/X* boards, for a maximum of 64 asynchronous ports.   
The devices are prefixed with the letter "i", and are located in /dev/term.  
DigiPrint transparent printer devices are in /dev and have the basename pri. 
 
Format used for port names 
 
i	Prefix for tty ports.  Devices are in /dev/term. 
pri	Base name for DigiPrint transparent printing. Devices are in /dev. 
1-4     Board ID_Driver supports up to four boards. 
a-p	Port ID of standard (not modem-controlled) port on PC/X* board. 
A-P	Port ID of "modem-controlled port" on the specified PC/X* board.  

Modem ports can only be opened when Data Carrier Detect (DCD) is active. 
For example, "/dev/term/i1d" specifies a standard device on the fourth port 
on board "1". "/dev/term/i1D" specifies the same port, but defines it as a 
modem device.  "/dev/pri1d" refers to a DigiPrint transparent printer on that 
port.


Building the New Kernel 

In this part of the installation procedure a new kernel is made. This
procedure is invoked automatically by the installation script. 
You will see the following (or similar) message: 
 
The UNIX Operating System will now be rebuilt. 
This will take a few minutes.  Please wait.
 
When the re-build is completed, the following message will be displayed: 
 
To complete the install/remove process a shutdown is now being initiated 
automatically. 
 
Make sure your floppy drive is empty.  If you are installing or removing 
controller boards, you may power down the system after shutdown is 
completed.

 
When the computer reboots, you should see messages which indicate the board is 
functioning.  Your screen might look something like this: 
 
pcxx:   PC/Xi   port: 0x00000320   mem:0x000D8000   8 ports   Ver 1.2.0


Enabling the New Ports 
Please refer to your UNIX System Administrator's Guide, under the Peripherals 
Setup section, for the details on how to enable serial ports.  The following
example shows how to set up serial ports for use with terminals: 

Connect terminals to the ports (using a null modem, if necessary) and test the 
connections to each terminal by entering the following command for each port 
added: 
date > /dev/term/i1a 
 
(Assuming the terminal is connected to i1a.) 
Please note that in the above, the "date" command is used as a simple test, to 
provide text output that can be redirected; there is no other significance to 
"date" in this test. Also note that the default settings for terminals is 9600
baud, 7 data bits, even parity and 1 stop bit. 

*If the date appears on the terminal's screen, the device is properly connected.
*If the date does not appear on the terminal's screen, then that terminal is
 not receiving data; check the power, cables, connections, etc. 
*If nonsense characters are printed on the terminal's screen, check the baud 
rates, data bits, stop bits, and parity setting on your terminal.  (UNIX
default parameters are 9600 baud, 7 data bits, 1 stop bit, and even parity.) 
Once you can redirect output to your screen with the test above, perform the 
following steps to enable the ports for monitoring by ttymon. 
 

1.	Log onto the console as super-user (root). 
 
2.	Enter: sysadm 

This will bring up the System Administration menu.  From this menu, select 
"Ports".  The Ports menu will now be displayed.  From the Ports menu, select
"Quick Terminal".  Now select "Add". You will now be shown a list of port
numbers that are currently being monitored for activity (the list may be
empty at this time). 
 
3.  Press <F2> ("Choices").  You will be shown a list of available ports. 
Use the arrow keys to move through the list of ports.  Press <F2> to mark
ports to be enabled (an asterisk will appear by the marked choices). 
IMPORTANT!  Do not select both modem and standard devices for the same 
port number (e.g. /dev/term/i1a and /dev/term/i1A). 
 
4.  When you have completed your selections, press <F3> ("Enter"). The list 
you saw in Step 3 will now include the ports you just selected. To accept the 
list, press <F3> ("Save"). 
 
5.	Now press <F3> again ("Continue"), press <F7> ("Cancel") to exit the 
Ports Setup menu.  The ports are now enabled. 
 
 
The default UNIX SYSTEM V REL 4 settings for these ports 
are: 9600, ixon, cs7, e, 1 (these defaults may have been 
changed by your system administrator).  These settings can be 
modified by going again to the Ports menu, selecting Ports 
Services, then selecting Modify.


Uninstalling the Device Driver 
1.  Log onto the console as super-user (root). 
 
2.  Enter: pkgrm 
 
3.  From the on-screen display, select the label corresponding to the
    PC/X* device driver. 
 
It will take some time for the new kernel to be built.  When it is finished,
perform a system shutdown. 
 

DigiBoard TTY Devices 
The DigiBoard PC/X* device driver supports three different UNIX devices on each 
line.  For example, on the first port of board number 1, there are three
devices: 
 
/dev/term/i1A 
The "modem" tty device, used for terminals, modems, printers, laboratory 
equipment, etc.  This is also sometimes referred to as a "dial-in" device. 
 
/dev/term/i1a	 
Standard device.  This is the same as i1A with the exception that the default 
handshake method is XON/XOFF, and that Data Carrier Detect need not be present 
 
/dev/pri1a 
The "Transparent Print Device" (DigiPrint), for use with the auxiliary printer
port of a terminal. Output directed to a pri device goes out the auxiliary
port of a terminal while the user continues to use the terminal normally. 

Error Messages 
The following error messages are generated by the driver: 
 
WARNING: pcxx: No board found at port 0x00000320 <1>. 
or 
WARNING: pcxx at port 0x00000320 not resetting <3>. 

What it means:	The board doesn't respond to reset. 
Action to take:		 
Make sure the board is fully seated in the computer's slot. 
Make sure the board's jumper settings and the device driver's settings match. 
Potential hardware problem. 
 
WARNING: pcxx: memory allocation error: port 0x00000320 <2>. 

What it means: The operating system would not allocate memory to the driver. 
Action to take: Adjust kernel resources. 
 
WARNING: pcxx: No memory at 0x000D0000 <4>. 

What it means: The driver cannot read the board's dual ported memory;
            or the board failed a test of its memory. 
Action to take: 
Make sure the board is fully seated in the computer's slot. 
Make sure the board's settings and the device driver's settings match. 
Make sure the jumpers or DIP switches are in their proper positions. 
Make sure that there is no memory contention with other devices. 
Potential hardware problem. 
 
WARNING: pcxx: port 0x00000320 failed diagnostics <5>. 
or 
WARNING: pcxx: port 0x00000320: BIOS failed <6>. 

What it means: The driver encountered an error executing on-board BIOS.  
 
Action to take: 
Make sure the jumpers or DIP switches are in their proper positions. 
Make sure there is no memory contention with other devices.  
Potential software problem. 
Potential hardware problem. 
 
WARNING: pcxx: FEPOS failed <7>. 

What it means: The driver encountered an error executing on-board FEP BIOS. 
Action to take: 
Make sure the jumpers or DIP switches are in their proper positions. 
Make sure there is no memory contention with other devices.  
Potential software problem. 
Potential hardware problem.