Software Installation and Operating Manual

                for

DigiCHANNEL COM/Xi~ SCO UNIX System V/386 Releases 3.2.0 - 3.2.4
                    SCO XENIX 286 and 386 Releases 2.2.3 - 2.3.4


Software Installation    SCO XENIX SCO Unix 

Installation of the device driver software
for SCO XENIX and SCO Unix is a four-part
procedure.  In Part One, a new kernel is
linked.  In Part Two, new devices for the
serial ports are made in the /dev directory,
and these devices are added to /etc/ttys
for SCO Xenix and /etc/initab for SCP Unix. 
In Part Three, a back-up copy of the current
kernel is made and the new kernel is copied
into the root directory.  Finally in Part
Four you boot the new kernel and enable the
communications ports for use with a
terminal.

Step 1.        Log onto the console as
               super-user (root).

Step 2.        Insert the DigiWARE diskette,
               and type:

               custom          [Press ENTER]

Step 3.        The system will now display
               the Custom Menu.  If the
               device driver has been
               previously installed, the
               Custom Menu lists DigiWARE. 
               If not, select Option 4 to
               add a supported product.  The
               system displays:

  Installing custom data files...

  Insert distribution volume 1 and press <Return> or enter q to quit:



Step 4.        Press <Return> and the system
               displays the following menu:

  1.   Install one or more packages
  2.   Remove one or more packages
  3.   List the available packages
  4.   List the files in a package
  5.   Install a single file
  6.   Select a new set to customize
  7.   Display current disk usage
  8.   Help

  Select an option or press q to quit:


           Select Option 1 to install
           DigiCHANNEL Software.  The
           system displays:

  Name     Inst   Size   DigiWARE for COM/Xi packages
  ------------------------------------------------------
  COMXI    NO     800    DigiCHANNEL COM/Xi async driver V4.4.0

           (Note that the ~size~ in the
           above display can vary from
           release to release.)   


 
          The system will then display:

  Enter the package(s) to install or enter q to return to the menu:
           Type:

               COMXI           [Press ENTER]


           The system will then display:

  Insert DigiWARE package volume 1 and press <return> or enter q to
  return to the menu:

           Volume 1 should still be in the
           disk drive.  Press <Return>. 
           The system will then display:

  Extracting files...

Step 5.        You must now answer a series
               of questions about the
               installation.  In each case,
               options will be presented
               and/or examples will guide
               you in answering the
               questions.  The driver may be
               installed by using one of
               four pre-configured versions,
               or may be installed in any
               other configuration.   You
               will see the screen:

  The DigiCHANNEL COM/Xi driver may be installed using one of the four
  suggested configurations listed below, or you may choose to create
  your own custom configuration.

  1) I/O Port=0x320, Memory Address=0x000D8000
  2) I/O Port=0x300, Memory Address=0x000D0000
  3) I/O Port=0x220, Memory Address=0x000C8000
  4) I/O Port=0x120, Memory Address=0x000C0000
  5) Custom or multiple board installation.
  6) Exit installation procedure.

  Please enter selection (1-6)? 

          When asked, select your con-
          figuration from the above list
          (1-6).  

          Note that options 1 through 4 are
          for installing single boards only! 
          If your are installing two, three,
          or four boards, or wish to set up
          one board with parameters
          different from those above, choose
          #5.  

          For any of the versions selected,
          the corresponding jumpers on the
          COM/Xi board must be set to match
          the parameters listed in the con-
          figurations above.  


          If you selected Option 5, the next
          prompts you will see will be for
          Custom Configuration Instructions. 
          If you answered 1 through 4, skip
          to Step 11 on page 25.

Step 6.    The software displays:

  Each DigiCHANNEL COM/Xi board requires an I/O port address and a 32K
  block of memory.  Please select these to avoid conflicts with other
  boards you may have installed in your system.

  How many DigiCHANNEL COM/Xi boards do you wish to install (1-4)? 
          Type in the number of COM/Xi
          boards you are installing.


Instructions 7, 8 and 9 are repeated for
each of the boards you specified in Step
6.

Step 7.    You must select a Port Address
           for each board.  The software
           displays the Port Address
           options. 

     The I/O port address choices, in hexadecimal, are:

     1) 1003) 1205) 2207) 320
     2) 1104) 2006) 300


  Please enter selection (1-7)? 
          Enter your selection by typing in
          one of the numbers shown above.


Step 8.        The next item requires the
               selection of the host
               starting address of the
               board's dual-ported memory. 
               Each board must have a unique
               Memory Address.  The software
               lists the available Memory
               Address options.

  The memory address choices, in hexadecimal, are:

       1)  0x00d8000
       2)  0x00d0000
       3)  0x00c8000
       4)  0x00c0000

  Please enter selection (1-4)? 
           When asked, enter your selection (1-4).


Step 9.        The software asks:

       Please indicate number of ports on board (4 or 8)? 
           Answer 4 or 8 as appropriate for
           the number of channels on the
           DigiCHANNEL board you are
           installing.

Step 10.       The software will now show
               you what you have chosen. 
               (The following is an example
               screen; yours may be
               different.)

  You have selected the following configuration:

     Board   I/O Address   Memory Address     Ports
     ---------------------------------------------------
       1        0x320        0x000D8000        8 

  Is this configuration acceptable (y or n)?

           If the information is correct,
           answer ~y.~  Otherwise, answer
           ~n~ and the software will let
           you start over again with Step
           5.


Step 11.       Finally, you need to select
               the Altpin setting.  This
               allows alternate wiring of
               the RJ-45 modular connectors. 
               The default for altpin is
               OFF, giving you the standard
               DigiBoard RJ-45 pinouts. 
               Setting altpin to ON enables
               the alternate RJ-45 pinouts. 
               (This is useful for 8-pin RJ-
               45 connectors.  See the main
               COM/Xi manual for more
               details, as well as page 58
               of this manual.)  The
               software asks:

The default setting for altpin is off.  
Is this acceptable (y or n)?
           Answer y or n as appropriate.


Step 12.       Installing DigiScreen


           DigiScreen is DigiBoard's
           multiple screen utility that
           allows a single physical
           terminal to be connected to
           several virtual terminal
           sessions (screens) at one time. 
           The software installation script
           gives you the option of
           installing it.

           If you have already installed
           DigiScreen with another
           DigiBoard product, there is no
           need to install it again, unless
           you wish to change the number of
           DigiScreen devices.

           DigiScreen is not available for
           the 286 XENIX operating system.


           The software asks:

Do you wish to install DigiScreen (y or n)?

           If you answer "n," proceed to
           page 25, Device Nodes.


Step 13.       The software continues:

Each session under DigiScreen requires a DigiScreen device.

How many DigiScreen devices do you wish to have installed
(max. is 256, default is 32): ?

           Answer with the number of
           DigiScreen devices you think
           will be adequate for all
           connected terminals.  Note that
           the default value will change
           according to the number of
           previously created DigiScreen
           devices you may have.


Step 14.         At this point, the
                 operating system asks:

  Do you wish to make new device nodes (y or n)?

           Most users will need to create
           the new devices at this time,
           and should answer ~y~ and
           proceed to Part Two, Creating
           New Devices.

           However, if you are an
           experienced XENIX user, you do
           have the option of skipping Part
           Two, the creation of new
           devices.  If you answer ~n~ you
           will proceed to Part Three:
           Installing the New Kernel.

Part Two:  Creating New Devices
     

This portion of the installation procedure
creates devices in /dev and edits /etc/ttys,
giving XENIX the information to use these
additional ports.  By default, these ports
are installed with device names ttyi11
through ttyi18, ttyi21 through ttyi28,
ttyi31 through ttyi38, and ttyi41 through
ttyi48.

The DigiCHANNEL driver will support up to
four boards, for a maximum of 32
asynchronous ports.  


Step 1.        The software displays:

     This script also installs the information needed by XENIX to use
     these additional ports.  The DigiCHANNEL COM/Xi async driver will
     support up to four boards for a maximum of thirty-two asynchronous
     serial ports.

  By default, the ports are installed as ttyi11 through ttyi48.

  Ports with modem control are installed as ttyI11 through ttyI48.

  DigiPrint ports are installed as pri11 through pri48.

  DigiPrint ports with modem control are installed as prI11 through
  prI48.

  Is this acceptable (y or n)?

  ~Yes~    Answer ~y~ if the default device
           names listed above (and on your
           console screen) are acceptable. 
           You may then proceed to Part
           Three:  Installing the New
           Kernel, as the remainder of this
           step asks for new names for the
           nodes and the DigiPrint ports.
  ~No~    If you answered ~n~ to the
          preceding question, enter the name
          you wish when the systems
          responds:

  Device names will be a base name followed by an i for base tty ports,
  or I for modem control ports, with the board number (1-4) and the port
  number (1-8) appended.  
  Please enter base name to use:
          The default printer names are
          pri11 through pri48. The
          installation program will now ask
          for an alternate name:

  Please enter DigiPrint name to use:


Step 2.    The software displays:

Do you wish to update /etc/ttys and /etc/ttytype (y or n) ?

          For a new installation, answer ~y~
          (yes).  For updates, answer ~n~ to
          preserve the current setup.  If
          you aren't  sure, answer y.~




At this point, you may proceed to Part
Three: Installing the New Kernel.
Format used for port names:

tty       Base name.  You may select a
          different one.  (Another default
          that you may change is pr for
          DigiPrint ports.)  The base name
          is followed by a lowercase ~i~
          for ports without modem control,
          and by an uppercase ~I~ for ports
          with modem control.

b         Board number (1 through 4
          possible, depending upon the
          number of boards installed.)

p         Port number on the individual
          board (1-8 for an eight-port
          COM/Xi board.)

Example 1:       If ~crt~ was the base
                 name,  Port 4 on the third
                 eight port board would be
                 crti34.

Example 2:       ttyI11 indicates that the
                 first port on the first
                 board has modem control
                 enabled.

Part Three:  Installing the New Kernel

The device driver software installation is
now complete, and the new kernel must be
installed.


Step 1.        You will see:

  The new kernel with driver modifications is in /usr/sys/conf/xenix.

  Do you want this kernel to boot by default (y or n)?

           If you type ~y~ you will see:

  The old kernel is installed in /xenix.old

  The new kernel is installed in /xenix

  Enter the following command to reboot your system and activate the new
  kernel:

  haltsys     <cr>

           If you type ~n~ you will see:

  Changes will not be reflected unless
  /usr/sys/conf/xenix is copied to /xenix.

Step 2.        The system displays:

  1.   Install one or more packages
  2.   Remove one or more packages
  3.   List the available packages
  4.   List the files in a package
  5.   Install a single file
  6.   Select a new set to customize
  7.   Display current disk usage
  8.   Help

  Select an option or enter q to quit:

           Enter q.

Step 3.        If you choose to have the new
               kernel boot by default, enter
               the following command to boot
               the new kernel:

               shutdown 0      [Press ENTER]


Step 4.        When the computer reboots,
               you should see messages which
               indicate the board is
               functioning.  Your screen
               might appear to look some-
               thing like this:

  device     address    vector   dma   comment
  -----------------------------------------------------
  %comxi     0x3200       -       -    mem=0x000D8000
                                       ports=8 
                                       COM/Xi V4.x.0

Part Four:  Enabling the New Ports SCO Xenix

Step 1.        With the cables connected to
               the terminals (using a null
               modem, if necessary), test
               the connections to each
               terminal by typing in the
               following for each port
               added:

               date > /dev/ttyi11

           (Assuming the terminal is
           connected to ttyi11.)

           (Please note that in the above,
           the ~date~ command is used as a
           simple test, to provide text
           output that can be redirected;
           there is no other significance
           to ~date~ in this test!)


           *   If the date appears on the
               terminal's screen, the device
               is properly connected.

           *   If the date does not appear
               on the terminal's screen,
               then that terminal is not
               receiving data; check the
               power, cables, connections,
               etc.

           *   If nonsense characters are
               printed on the terminal's
               screen, check the baud rates,
               data bits, stop bits, and
               parity setting on your
               terminal.  (XENIX default
               parameters are 9600 baud, 8
               data bits, 1 stop bit, and no
               parity.)

           Once you can redirect output to
           a terminal with the test above,
           you can continue the following
           step to enable that port.

Step 2.          To activate a port for use
                 with a terminal, type the
                 following command:

                 enable ttyi11

           (If you've assigned a new base
           name, replace the ~tty~ above
           with the name you chose.)

           The above command will cause a
           login prompt to be sent to the
           terminal connected to ttyi11. 
           To activate the other ports,
           repeat the enable command with
           the appropriate port name.



Un-Installing the SCO XENIX Device Driver


The DigiBoard DigiCHANNEL device driver
software can be removed from the kernel by
using the program custom.  Again, the
Development Kit is not required, although
the link kit must be installed.

Removing the driver from the kernel is a
two-part process.  First, the driver
references are removed from the system
configuration files.  Secondly, a new kernel
is linked, and copied to the root directory.

Enter the following commands to un-install
the device driver software:


Step 1.        Log onto the console as
               super-user (root), and enter
               the following command:

               custom          [Press ENTER]


Step 2.        Enter the proper number for
               the DigiWARE for COM/XI
               device driver software.

Step 3.        The system displays:

     1.   Install one or more packages
  2.   Remove one or more packages
  3.   List the available packages
  4.   List the files in a package
  5.   Install a single file
  6.   Select a new set to customize
  7.   Display current disk usage
  8.   Help

  Select an option or enter q to quit:

           Select Option 2 to remove the
           driver.  The system will
           display:

     Name     Inst   Size   DigiWARE for COM/Xi Packages
  ------------------------------------------------------------
  COM/Xi   YES    800    DigiCHANNEL COM/Xi async driver V4.x.0

           (Note that the ~size~ in the
           above display can vary from
           release to release.)   


Step 4.        The system will then display:

     Enter the package(s) to remove or enter q to return to the menu:
           Type:

               COMXI           [Press ENTER]


Step 5.        Next, the software asks:

Do you wish to remove DigiScreen devices (y or n)?
Removing DigiScreen devices will affect ALL DigiBoard Drivers.


Step 6.        You will see:

     The new kernel with driver modifications is in
  /usr/sys/conf/xenix.

  Do you want this kernel to boot by default (y or n)?

           If you type ~y~ you will see:

     The old kernel is installed in /xenix.old

  The new kernel is installed in /xenix

  Enter the following command to reboot your system and activate the new
  kernel:

  haltsys     <cr>

           If you type ~n~ you will see:

  Changes will not be reflected unless 
 /usr/sys/conf/xenix is copied to /xenix.

Step 7.        The system displays:

  1.   Install one or more packages
  2.   Remove one or more packages
  3.   List the available packages
  4.   List the files in a package
  5.   Install a single file
  6.   Select a new set to customize
  7.   Display current disk usage
  8.   Help

  Select an option or enter q to quit:

           Enter q to quit.


Step 8.        Remove the perms file:

               rm /etc/perms/comxi[press ENTER]



Step 9.        If you choose to have the new
               kernel boot by default, enter
               the following command to boot
               the new kernel:

               shutdown 0      [Press ENTER]

Part Four:  Enabling the New Ports SCO Unix

Step 1.        With the cables connected to
               the terminals (using a null
               modem, if necessary), test
               the connections to each
               terminal by typing in the
               following for each port
               added:

               date > /dev/ttyi11

           (Assuming the terminal is
           connected to ttyi11.)

           (Please note that in the above,
           the ~date~ command is used as a
           simple test, to provide text
           output that can be redirected;
           there is no other significance
           to ~date~ in this test!)


           *   If the date appears on the
               terminal's screen, the device
               is properly connected.

           *   If the date does not appear
               on the terminal's screen,
               then that terminal is not
               receiving data; check the
               power, cables, connections,
               etc.

           *   If nonsense characters are
               printed on the terminal's
               screen, check the baud rates,
               data bits, stop bits, and
               parity setting on your
               terminal.  (Unix default
               parameters are 9600 baud, 8
               data bits, 1 stop bit, and no
               parity.)

           Once you can redirect output to
           a terminal with the test above,
           you can continue the following
           step to enable that port.

Step 2.        The Terminal Control Database
               must be updated to include
               the new devices.  Add the
               DigiCHANNEL device
               information using the fol-
               lowing SCO UNIX sysadmsh
               command sequence:

           AccountsTerminal:Create

           Fill in the required information
           on the form displayed.


Step 3.          To activate a port for use
                 with a terminal, type the
                 following command:

                 enable ttyi11

           (If you've assigned a new base
           name, replace the ~tty~ above
           with the name you chose.)

           The above command will cause a
           login prompt to be sent to the
           terminal connected to ttyi11. 
           To activate the other ports,
           repeat the enable command with
           the appropriate port name.

Un-Installing the SCO Unix Device Driver

The DigiBoard DigiCHANNEL device driver
software can be removed from the kernel by
using the program custom.  Again, the
Development Kit is not required, although
the link kit must be installed.

Removing the driver from the kernel is a
two-part process.  First, the driver
references are removed from the system
configuration files.  Secondly, a new kernel
is linked, and copied to the root directory.

Enter the following commands to un-install
the device driver software:

Step 1.        Log onto the console as
               super-user (root), and enter
               the following command:

               custom          [Press ENTER]


Step 2.        When the operating system
               menu asks, choose REMOVE.


Step 3.        Select DigiCHANNEL COM/Xi
               Software.  The software will
               respond with:

Removing DigiCHANNEL COM/Xi intelligent async serial driver.

Step 4.        Next, the software asks:

Do you wish to remove DigiScreen devices (y or n)?
Removing DigiScreen devices will affect ALL DigiBoard Drivers.

Step 5.        When asked if you wish to
               create a new kernel, answer
               ~y~ (yes).


Step 6.        You will see:

  Do you want this kernel to boot by default (y or n)?

           If you type ~y~ you will see:

  The old kernel is installed in /unix.old
  The new kernel is installed in /unix

           If you type ~n~ you will see:

  Changes will not be reflected unless /etc/conf/cf.d/unix is copied to
  /unix.

Step 7.        The system displays:

     Do you want the kernel environment rebuilt?

           Answer ~y~ (yes).  You will see:

  The kernel has been successfully linked and installed.  To activate
  it, reboot your system.


Step 8.        Remove the perms file:

               rm /etc/perms/comxi{Press ENTER]

Step 9.        Enter the following command
               to boot the new kernel:

               shutdown -y -g0 [Press ENTER]