Release Notes 93000221AD

for

PORTSERVER II Operating System

40001260AC

Version 3.1.10

Software Manual P/N 92000246C

Software Manual P/N 92000271B

December 21, 2001

I. Introduction

These release notes provide information on PortServer II OS version 3.1.10.

II. Summary

A.   Pre-3.0 Incompatibility Notice.

B.   Pre-Rev K Model ROM Limitations.

C.   Limitations for Systems with 2 Mbytes of Memory.

- Upgrading flash ROM.

- Bug fixes in this release.

III. Details

- Pre-3.0 Incompatibility Notice

This version (v3.1.10) of the PortServer II OS is incompatible with versions older than v3.0.  Certain parts of the non-volatile storage formats used to store configuration information have been changed.  Consequently, if you want to use this version of the OS and preserve your current configuration, you must use the ‘cpconf ‘command to save your configuration to a host and then reload it once the new version of the PortServer II OS has been installed.

B.   Pre-Rev K Model ROM Limitations

The addition of Frame Relay to v3.0 and later have caused the size of the boot image to exceed the space available in the PortServer II flash ROM for units built prior to the Rev K models.  Consequently, if you want to use v3.0 or later OS with these older units, you must do one of the following:

- Boot PortServer II via TFTP over the Ethernet port.

- Acquire a smaller version of the OS, which does not have Frame Relay, this is available from the Digi ftp site.

Note: Versions above and including v3.1.0 will no longer be available in the smaller non-frame version.

C.   Limitations for Systems with 2 Mbytes of Memory

Testing has determined that the PortServer II's previously standard 2 Mbytes of installed memory is inadequate in the following instances and is likely to require an expansion to at least 4 Mbytes.

- Full 64 port configurations in which more than 50 asynchronous and/or TCP users are simultaneously using the PortServer II.  This includes users accessing the PortServer II via the Ethernet connection or any type of connection using the serial ports.

- Sites with heavy traffic on serial ports.  The problem is simply throughput – degradation of performance may indicate that additional memory is called for.

D.  Upgrading Flash ROM

In some instances parameters from previous releases (e.g. v3.1.9) may not translate properly into v3.1.10. In order to insure that the parameters are correct the user can save their parameters from the previous releases by doing a ‘cpconf tohost’ and reload the parameters back into the PortServer II after 3.1.10 is loaded.

- The recommended procedure for upgrading Flash ROM is:

- Obtain the new version of the software from Digi and place it on your TFTP server.

- Save your current configuration using ‘cpconf’.  This is recommended to maintain a backup of your current configuration when re-writing a sizable portion of flash.

- Boot with the new OS (v.3.1.10) via TFTP by using ‘set config boothost=<hostip> bootfile=<filename> tftpboot=yes’, and then reboot your PortServer II.  See command ‘set config’ in User's Guide and Reference Manual for more details.  This step ensures that you have a good copy of the new OS, and also that you can still boot your PortServer II in the unlikely event that your flash image gets corrupted in the process of writing it.

- After booting your PortServer II via TFTP, load the new OS onto the flash ROM by using the command ‘boot load=<host>:<filename>’.  If all goes well, the PortServer II will reply “The image now in flash memory appears valid.”

- Reset the PortServer II to factory default by using either the two-button reset or ‘boot action=eewrite’.

Note: ‘boot action=eewrite’ will leave some IP configurations intact to insure the PSII can be reached and booted from the network.

- Configure the IP configuration settings. As a minimum define the PortServer II’s IP Address and Submask.

- Load the ‘cpconf’ files from your TFTP server. Note: This may generate warnings.

  - Bug Fixes

- 5826: Idle Timeouts and Session Timeouts defined for user sessions were not working correctly.

- 6933: The login username was not echoed during a passthrough login.

- 7310: Telnet Sub-option Negotiation was happening before Option Negotiation concluded.

- 7498: The file transfer of a file ending with a FF (i.e. an incomplete last line) could cause the PortServer to reboot. This issue has been fixed.

- 7530: Grammatical errors in various warning messages have been corrected.

- 7535: Spelling errors in various warning messages have been corrected.

- 7633: Autoconnect sessions were incorrectly being assigned escape sequences, these types of connections do not require the assignment of an escape sequence.

- 7652: A passthrough login displayed the banner message 'local authentication' which could not be toggled with the ‘set login verbose=off’ command.

- 7776: A passthrough login’s Idle Timeout and Session Timeout features were not working correctly.

- 7830: The SNMP ‘get request’ and ‘set request’ community strings were getting initialized to ‘public’ and ‘private’, respectively, each time the SNMP daemon was started.